BookSense XT User Manual

# English Manual

# For Software Version 3.0

# January 2013.

# HIMS Inc.

4616 W. Howard Lane, Ste 960 Austin, TX 78728

Phone: 888-520-4467

Fax: 512-837-2011

Email: support@hims-inc.com

# About BookSense XT

Thank you for purchasing the BookSense XT. This guide contains all the information you will need to get started with your new BookSense XT.

HIMS is proud to introduce the BookSense XT, a powerful digital-talking book portable device. The BookSense XT is designed as an advanced high-performance DAISY player.

The BookSense XT is a digital audio player that is manufactured by HIMS International Corporation, the creator of the popular SENSE product line. It is a very convenient, portable device which can play digital books, audio files, text files, and DAISY content. You can use the built-in digital recorder to record various items, such as lectures, music from the FM radio, and even record from external audio sources using the line-in mode.

The BookSense XT is the more advanced model of the BookSense and offers three additional features BookSense XT not included in the BookSense. Those three features are 4GB of built-in storage space (to allow data, music, and other files to be saved without using an external memory card), built-in FM radio, and Bluetooth.

With the model of the BookSense XT, if you use a Bluetooth headset, there are no wires creating a tangled mess, allowing you to enjoy the freedom provided by the wireless Bluetooth connection.

# Copyright 2011. All RIGHTS reserved, HIMS International Corporation.

This User Manual is protected by copyright belonging to HIMS, with all rights reserved. The User Manual may not be copied in whole or part, without consent from HIMS.

# TABLE OF CONTENTS

1. Overview BookSense XT	1

1.1 What’s in the package?	1

1.2. Hardware Specifications	1

1.3. Physical Description of BookSense XT	2

1.3.1 Front Face of the Device	3

1.3.2 Back of the Device	3

1.3.3 Left Side of the Device	3

1.3.4 Right Side of the Device	3

1.3.5 Top Side of the Device	4

1.3.6 Bottom Side of the Device	4

1.4 Turning the Device On after purchasing	4

1.5 Inserting or Removing the Battery	4

1.6 Turning the Device On/Off	5

1.7 Charging BookSense XT	5

1.8 Inserting or Removing the SD CARD/USB Memory/USB CD-ROM	5

1.8.1 Inserting or Removing the SD CARD	5

1.8.2 Inserting or Removing the USB Memory/CD-ROM	6

1.9 Connecting to PC	6

2. Basic Functions and Structures	7

2.1 Folders used in the BookSense XT	7

2.2 Switching Mode	7

2.3 Changing Volume	7

2.4 Navigating through Files and Folder	8

2.5 Deleting File or Folder	8

2.6 Moving to the specific File or Folder	9

2.7 Switching the current storage device	9

2.8 Copying Files Among storage devices	9

2.9 Using Menus, Dialogs, Combo Boxes, Edit Boxes	10

2.10 Checking Battery Status	11

2.11 Setting Date & Time	12

2.12 Checking Date &Time	13

2.13 Changing Voice	13

2.14 Set sleep timer	13

2.15 Bluetooth On/Off	14

2.16 Hold Switch	14

2.17 Marks used in BookSense XT	14

2.18 Stop the voice	14

3. Using Help Mode	15

4. Media	16

4.1 What is supported in the Media?	16

4.2 Playing Audio Files	16

4.2.1 Playing selecting Audio Files	16

4.2.2 Remembering the last position	17

4.3 Pause	17

4.4 Changing the Unit to Move By	17

4.5 Move by 1 track	18

4.6 Move by 5 tracks	18

4.7 Moving to First or Last track	18

4.8 Moving by Time	18

4.9 Changing preamp	18

4.10 Moving by Mark	19

4.11 Section Repetition	19

4.12 Marks	19

4.12.1 Inserting a Mark	20

4.12.2 Inserting a Voice memo	21

4.12.3 Inserting a Highlight mark	22

4.12.4 Moving to a Mark	23

4.12.5 Deleting a Mark	24

4.13 Adjusting the Playing Speed	25

4.13.1 Play Slower	25

4.13.2 Normal speed	25

4.13.3 Play Faster	25

4.14 Setting Moving Mode to Time	25

4.15 Shuffle	26

4.16 Move within a File via a Percent	26

4.17 Repeating a File	26

4.18 Equalizer Settings	27

4.19 Saving the Playlist	27

4.20 Undo & Redo in Media Player	27

4.21 Checking the Information of the current file	27

4.22 Checking the Tag Information of the current file	28

4.23 Using the Menu in the Media	28

4.23.1 Equalizer Settings	28

4.23.2 Playback Settings	28

4.23.3 Select Playlist	30

4.23.4 Saving the Playlist	32

4.23.5 Mark information	32

4.23.6 Add to alarm Melody	33

5. DAISY	34

5.1 What is supported in the DAISY Player	34

5.2 How to play DAISY content	34

5.3 Pause	35

5.4 Changing the Unit to Move By	35

5.5 Moving by Phrase	35

5.6 Moving by Paragraph	35

5.7 Moving by Heading	35

5.8 Moving to Beginning or End of book	36

5.9 Moving by Time	36

5.10 Changing preamp	36

5.11 Moving by Mark	36

5.12 Moving by Level	37

5.13 Moving by Page	37

5.14 Additional units to Move by	37

5.15 Marks	38

5.15.1 Inserting a Mark	38

5.15.2 Inserting a Voice memo	39

5.15.3 Inserting a Highlight mark	40

5.15.4 Moving to a Mark	41

5.15.5 Deleting a Mark	42

5.16 Adjusting Playing Speed	43

5.16.1 Play Slower	43

5.16.2 Normal Speed	44

5.16.3 Play Faster	44

5.17 Setting the Moving Mode to Time	44

5.18 Moving to a Page	44

5.19 Moving to a Heading	45

5.20 Undo & Redo in DAISY Player	45

5.21 Checking the Content Information	45

5.22 Checking the Status of the Content Information	46

5.23 Using the Menu in the DAISY	46

5.23.1 Play DAISY contents with audio + text file	47

5.23.2 Reading Page Tag	47

5.23.3 Mark information	47

5.23.4 Import contents from CD-ROM or NLS cartridge	48

6. Document Reader	49

6.1 What is supported in the Document Reader?	49

6.2 Playing a Document File	49

6.3 Pause	49

6.4 Changing the Unit to Move By	50

6.5 Moving by Page	50

6.6 Moving by Paragraph	50

6.7 Moving by Heading Level	50

6.8 Moving by Line	51

6.9 Moving by Sentence	51

6.10 Moving by Word	51

6.11 Moving by Character	51

6.12 Moving by Phonetic	51

6.13 Moving by Mark	51

6.14 Search Word	52

6.15 Marks	52

6.15.1 Inserting a Mark	52

6.15.2 Inserting a Voice Memo	53

6.15.3 Inserting a Highlight mark	54

6.15.4 Moving to a Mark	55

6.15.5 Deleting a Mark	56

6.16 Adjusting Playing Speed	57

6.16.1 Decrease Speed	57

6.16.2 Normal Speed	57

6.16.3 Increase Speed	58

6.17 Moving to a Page	58

6.18 Moving by Percent	58

6.19 Undo & Redo in Document Reader	59

6.20 Checking the Status of Content Information	59

6.21 Using Menu in the Document Reader	59

6.21.1 Recent Documents	59

6.21.2 Mark Information	60

6.21.3 Page Settings	60

7. Radio	61

7.1 Scanning to the Previous/Next Frequency	62

7.2 Moving to the Previous/Next Frequency by 0.1 MHz	62

7.3 Jump to Specific Frequency	62

7.4 Mute/Unmute	62

7.5 Moving to the Previous/Next Added Preset	62

7.6 Adding Presets and Moving to Presets	63

7.6 Changing the Frequency scanning Sensitivity	63

7.7 Deleting Presets	63

7.8 Listening to the Radio via the Internal Speakers	63

7.9 Checking the Channel Information	64

7.10 Recording a Radio Broadcast	64

7.11 Adding Marks during Radio recording	65

7.12 Using Menu in the Radio	65

7.12.1 How to set the Internal Speakers	65

7.12.2 Radio Recording Settings	65

7.12.3 Preset	66

7.12.4 Adjusting the Frequency scanning Sensitivity	67

8. Recording	68

8.1 Recording via the Internal Microphone	68

8.2 Recording via an External Microphone	69

8.3 Recording via Line-in	69

8.4 Adding Marks during Recording	70

8.5 Recording DAISY Books	70

8.5.1 Making a DAISY Recording	70

8.5.2. Pause	70

8.5.3. Close	71

8.5.4. Insert Mark	71

8.5.5. Insert Heading	71

8.5.6. Insert Phrases	71

8.5.7. Insert Page	72

8.5.8. Play Recording	72

9. Global Options	75

9.1 Alarm Settings	75

9.1.1 Review current Alarm	75

9.1.2 Set Alarm	76

9.1.3 Delete the Alarm	77

9.2 Date and Time Settings	77

9.2.1 Check Date and Time	77

9.2.2 Set Date and Time Notification	78

9.2.3 Set Date and Time	78

9.3 Voice Settings	79

9.4 Recording Settings	80

9.5 Check System Status	81

9.6 Bluetooth Options	81

9.6.1 Turning on Bluetooth & Connecting a Bluetooth headset	82

9.6.2 Connecting a Bluetooth headset	83

9.6.3 FTP Service	84

9.6.4 Turning off Bluetooth	84

9.6.5 Disconnecting a Bluetooth headset	85

9.6.6 Unpairing a headset	85

9.7 Set Sleep Timer	86

9.8 Power save mode settings	86

9.9 Mark alert settings	87

9.10 Format Storage Device	87

9.11 Set Current Storage Device	88

10. Advanced options	89

10.1 Upgrade	89

10.2 Backup/Restore settings	89

10.3 Effect sound settings	90

11. Calculator	91

11.1 Using the Calculator	91

11.2 Inputting and operating the four fundamental arithmetic	91

11.3 Using the help mode of Calculator	93

12. Troubleshooting Guide	93

12.1 The BookSense XT will not turn on	93

12.2 The BookSense XT stops responding	93

12.3 Having trouble with Scanning Radio Channels	93

12.4 No sound when using Bluetooth	94

12.5 No Sound from Internal Speakers or Earphones	94

13. Warranty	95

14. Contact Information	96

# 1. Overview BookSense XT

## 1.1 What’s in the package?

The package contains following items:

- BookSense XT

- Battery pack

- AC adaptor (5V DC, 2A)

- Earphone

- SD Card (8GB)

- USB Cable to connect BookSense XT to a PC

- USB Gender cable

- Pouch

- Lanyard

- User Manual CD

- Quick Guide Manual (Braille/Regular print)

## 1.2. Hardware Specifications

- MP3 Recording (Internal, External, Line-In, FM)

- USB OTG (Mini AB type connector)

- SD Card Slot

- Internal Memory : 4GB

- FM Radio

- Bluetooth 2.0 (Supports stereo Bluetooth headset)

- Stereo Earphone Jack (3.5 pie)

- Stereo Microphone Jack (3.5 pie, available for Line-In or External MIC.)

- Internal Stereo Speakers

- Internal Mono Microphone

- Detachable battery (Lithium Polymer, 3.7V)

  - 12 hours continuous of use.

  - 2.5 hours charging time using AC adapter, 5 hours charging time using USB cable.

- DC-Jack(3.5 pie)

- Size: 47mm(W) x 108mm(L) x 18.5mm(H)

- Weight: 115g/0.25 lbs

## 1.3. Physical Description of BookSense XT

### 1.3.1 Front Face of the Device

If you place the BookSense XT on a flat surface, such as a desk, the front of the device is oriented up. If you place your hand on the unit, and feel toward the top side of the BookSense XT, you will eventually feel a rough section toward the very top portion of the front. The rough section is the speaker and right below it is “DATE & TIME” button. The navigation buttons are located below “DATE & TIME” button. These buttons include the UP, DOWN, LEFT, and RIGHT buttons with the MENU button in the center of the four buttons. Beneath the navigation buttons, there is a numeric key pad, with 3 columns and 4 rows and a raised dot on the number 5 button. You can think of this key pad similar to the keypad found on a phone. The left key on the bottom row is the CANCEL button and the key on the bottom right is the OK button. The battery status LED is under the CANCEL button and the built-in microphone is under the OK button. The zero is located in between the CANCEL and OK buttons.

### 1.3.2 Back of the Device

The battery compartment is located on the back of the device. To insert the battery please refer to 1.5 Inserting or Removing the Battery. “Battery Lock Switch” is on the top center of the battery compartment.

### 1.3.3 Left Side of the Device

Starting from the top and moving down, you will find the MODE, volume up, and volume down buttons on the left side of the device. The SD memory card slot is located beneath these three buttons.

### 1.3.4 Right Side of the Device

The top two buttons are the PLAY and RECORD buttons, with the hold switch right below them. The PLAY button is also used as the power button. To use the PLAY button to turn on and off the device, please refer to section 1.6 Turning the Device On/Off.

Beneath the hold switch, there is a small hole for the reset button, which is used when the device malfunctions or stops working. You can use a toothpick or the end of a paperclip to press the reset button. Be careful when pressing the reset button because pressing too hard or using an end too small may damage the device if you are not careful. If you have difficulty pressing the reset button, then you can also reset the device by removing and re-inserting the battery. When you remove and re-insert the battery, you must wait at least 10 seconds before inserting the battery.

### 1.3.5 Top Side of the Device

The headphone and microphone jacks (1/8-inch) are respectively located on the right and left side of the center strap holder.

### 1.3.6 Bottom Side of the Device

The AC adapter jack is located on the left and the USB OTG port is located on the right of the bottom surface. Plug-in the end of the power adapter into the power input jack and the other end into an electrical outlet to charge the battery. The USB OTG port can be used to access a USB flash drive, transfer files between a PC and the BookSense XT, and can be used to charge the device using a USB cable.

## 1.4 Turning the Device On after purchasing

To turn on the device for the first time, you need to connect the AC adapter to the device. Connect one end of the AC adapter to the BookSense XT, and the other end to an electrical outlet. Once you connect the BookSense XT to the AC adapter, you will hear a sound indicating the BookSense XT is booting up. The Media Player is start running after 20 seconds. Once powered on, insert the battery and start using the BookSense XT. Please refer to 1.6 Turning the Device On/Off.

## 1.5 Inserting or Removing the Battery

To insert the battery, find the proper battery orientation. Front side has smooth surface with company logo engrave on it. The back side has rough surface with two tabs on either side at the bottom. Insert the bottom edge of battery first, making certain the bump fits in the appropriate opening, and snap the top edge in place. The smooth front side surface must be facing up.

The battery is designed to fit in only the correct orientation. If you feel any resistance it is likely you have the battery upside down. Secure the battery compartment by sliding the door back on, ensuring it locks in place.

To remove the battery, find “Battery Lock Switch” on the top center of the battery compartment and hold pushing up the switch; pull the battery out compartment by sliding the door.

## 1.6 Turning the Device On/Off

To turn on the device, press and hold down the PLAY button for more than 2 seconds, which is located on the right side of the device, near the top corner, and then you will hear a sound.

To turn off the device, press and hold down the PLAY button for more than 2 seconds again, then you will hear a sound.

## 1.7 Charging BookSense XT

To charge the battery, you need to connect BookSense XT to the main adapter or to a computer using the supplied USB cable. Follow these steps:

- To charge the battery using main adapter, plug the supplied AC adapter into the AC adapter jack on the bottom left edge of the device. A full recharge takes about 2.5 hours.

- To charge the battery using the USB connection, plug the USB OTG cable into the USB OTG port on the bottom right edge of the device. Then the wider end of the cable should be connected into USB port on your computer. If the BookSense XT is turned on, a full recharge takes about 10 hours and when it is turned off, a full recharge takes about 5 hours.

- While charging, LED located below the CANCEL button will glow red and when it’s fully charged, it will glow green and you will hear “Battery charging completed” sound even the device is turned off.

## 1.8 Inserting or Removing the SD CARD/USB Memory/USB CD-ROM

### 1.8.1 Inserting or Removing the SD CARD

To insert and remove the SD card, follow these steps:

- Hold the device facing you. The SD card slot is located on the left side of the device.

- One corner of the SD card is cut at a 45 degree angle.

- This cut corner should be at the top right when you insert the card into the device slot. If the card is not oriented properly it will resist insertion.

- Gently push the card into the slot until it clicks into place. Do not use excessive force. Only slight pressure is required to lock the SD card into place. Once its lock in place, you will hear a sound.

- To remove the card, push right on the left bottom edge to release it. Then pull it out.

Note: If the large capacity of SD card is inserted, the BookSense XT takes a little bit time to recognize it, and the BookSense XT makes the beep sound while recognizing it.

### 1.8.2 Inserting or Removing the USB Memory/CD-ROM

To insert and remove the USB Memory/CD-ROM, follow these steps:

- Connect USB to USB gender, USB gender to USB OTG port.

- To connect USB CD-ROM drives, procedure are same as USB Memories. However, device can recognize CD containing Daisy content only. CD media with other content cannot be recognized by the device.

Note: If the large capacity of USB Memory is inserted, the BookSense XT takes a little bit time to recognize it, and the BookSense XT makes the beep sound while recognizing it.

When you connect the CD-ROM to BookSense XT, you must supply the power for CD-ROM through its power port. If not, BookSense XT may not recognize the CD-ROM.

Inserting a SD card, USB Memory and CD-ROM to incorrect direction could be a cause of fault to BookSense XT and external memory.

## 1.9 Connecting to PC

To connect BookSense XT to your PC, connect one end of the long USB cable to the USB OTG port on the bottom right edge of the BookSense XT and the other end to your PC’s USB port. Windows will recognize the BookSense XT flashdisk and SD card as a USB drive. You can then use Windows Explorer to transfer files back and forth. If the SD card is not inserted, the second drive will not be displayed. When you enter the “BOOKSENSE” drive, there is “RECORD”, “RADIO”, “AUDIO BOOKS”, “PODCASTS”, “MUSIC”, “Misc Audio”, “DOCUMENTS”, and “DAISY” folders. Please refer to 2.1 Folders used in the BookSense XT. While transferring file, the BookSense XT cannot be used. (Note: But the charging is proceeded automatically.)

Each folder contains “Playlist”, and “Mark” folders. These folders cannot be shown at the BookSense XT. So do not save any files into these folders and you can’t edit or cut files from these folders.

# 2. Basic Functions and Structures

## 2.1 Folders used in the BookSense XT

Following folders are shown in the flashdisk:

- RECORD: Folder which contain the recorded files of voice or Line-in through the “Media” program.

- RADIO: Folder which contains the recorded files of live radio channel recordings through the “Media” program.

- AUDIO BOOKS: Folder which contains the audio book and other audio files.

- PODCASTS: Folder which contains the audio file from the Internet through the “Media” program.

- MUSIC: Folder which contains music files that you want to play through the “Media” program.

- Misc Audio: Folder which contains files that were created using audio file such as mp3 you want to play through the “Media” program.

- DOCUMENTS: Folder which contains files that you can read through the “Document Reader” program.

- DAISY: Folder which contains daisy books to use with the “Daisy” program, you must make folders for each daisy books. But “NFB NewsLine”, “NLS”, “RFB&D”, and “Bookshare” folders are located under the DAISY. If you save other content without making folders, device won’t be able to locate the books.

## 2.2 Switching Mode

When the BookSense XT is on, pressing the MODE button to toggle through Media, Daisy, Document Reader, and Radio. Once you change the Mode, file lists for each folder can be shown. If you change to different mode while in action, action will resume when you come back to previous mode.

## 2.3 Changing Volume

Use volume UP or DOWN button to raise or lower the volume between 1~ 21. Default setting is 16. When you adjust the volume while playing, volume is adjusted without any notification. Only when it’s adjusted to default setting (16), it will notify the user by beep sound. However, device announces the volume status when you are pause or idle stage. The BookSense XT allows you to adjust volume both earphones and internal speakers. When you connect earphones to the device, you can adjust the volume which comes from earphones. Removing earphones, you can adjust the volume which comes from internal speakers.

## 2.4 Navigating through Files and Folder

Here is how to navigate through files and folders.

- Move to next file or folder: Press the DOWN button.

- Move to previous file or folder: Press the UP button.

- Open sub folder: Press the RIGHT button.

- Move to higher level folder: Press the LEFT button.

- Announce File size and path: Press number 0.

- Play file: Press the PLAY or OK button.

- Toggle between male and female voice: Press number 5 button for more than 2 seconds.

- Move up 5 items in file list: Press number 1 button.

- Move down 5 items in file list: Press number 4 button.

- Move up 10 items in file list: Press number 2 button.

- Move down 10 items in file list: Press number 5 button.

- Move to top of file list: Press number 3 button.

- Move to bottom of file list: Press number 6 button.

- Move to specific number of file list: Press number 8 button and enter the number that you want to move to.

- Select all files or folders (Media mode only): Press number 7 button.

- Select/Unselect file or folder (Media mode only): Press number 9 button.

- Cancel all selected lists (Media mode only): Press the CANCEL button.

- Delete file or folder: Press number 3 button for more than 2 seconds.

- Change the disk: Press number 0 button for more than 2 seconds.

## 2.5 Deleting File or Folder

To delete the file or folder in file list, follow these steps:

- Move to file or folder that you want to delete.

- Press number 3 button for more than 2 seconds. Then “Delete (file or folder name)? Yes” is announced.

- Press the OK or MENU button. Then “Delete completed” is announced.

If you don’t want to delete it, press the LEFT or RIGHT button to select “No” then press the OK button.

Note: If the SD card is write protected, when you press the number 3 button for more than 2 seconds, the BookSense XT says, “Deleting is not possible because the SD card is write protected.”

## 2.6 Moving to the specific File or Folder

To move to specific number of file list, follow these steps:

- In the file or folder list, press number 8 button.

- Then “Enter the item number to move to, edit box” is announced and you need to enter the number that you want to move to.

- Press the OK or MENU button.

To cancel moving to the specific file or folder, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

## 2.7 Switching the current storage device

BookSense XT displays a file list of the designated storage device. If you want to use the other storage device, please refer to 9.11 Set Current Storage Device.

You can switch between two storage devices to press 0 button more than 2 seconds. Then BookSense XT shows a list of file & folder in usable storage device by rotating and can be used on that storage device.

## 2.8 Copying, Searching, and Creating Files/Folders Among storage devices

At times, you may wish to copy or move files from one storage device to another on the BookSense. Please use the following methods to copy and paste files from one folder/drive to another.

1. To copy selected files and folders to the clipboard, press the Menu key, navigate to “Copy” with the DOWN arrow, and press “OK”.

2. Navigate to the drive/folder in which you want to paste the files.

3. Press “Menu” and use the UP or DOWN arrow to navigate to “Paste” and press the “OK” button.

A. While pasting, if you press 0, press the up or down arrow and Booksense announces the progress of the copy as a percentage. If you press and hold 0, BookSense announces the file name and its number in the list of files being copied.

B. While pasting, if you press the cancel key, BookSense prompts you to be sure you want to cancel the copy. If you press and hold, BookSense cancels paste without prompting.

4. If files are copied to the clipboard, the menu contains a check clipboard item. Use this menu item to get a list of files/folders on the clipboard. When checking the clipboard, if you press and hold number 3, the clipboard is cleared.

5. From a file/folder list, press and hold the number 8 to open the “Search” dialog. Type all or part of a file/folder name to search for using the text entry method described in the next section. Press the “Left” or “Right” arrow to move to the previous/next item matching your search term.

You can also create folders on your Flashdisk, SD card, or connected USB device.

To create a new folder, press “Menu” and use the arrow keys to navigate to “New folder”. Type the folder name in the edit box using the text entry method described in the next section and press “OK”.

Note: When creating a folder, you can use only the following symbols in the folder name: “. ! [ ] – _”

## 2.9 Using Menus, Dialogs, Combo Boxes, Edit Boxes

Each program mode has its own corresponding menus. Press the MENU button to activate the menu in the current program.

- Move to Next/Previous Menu item: UP/DOWN button.

- Execute Item/Open sub Menu: RIGHT, OK or MENU button.

- Exit Sub Menu: LEFT button.

- Close Menu: CANCEL button.

Some menus contain sub menus. Use procedures 2 and 3 to enter and exit sub menus. However, if there is no sub menu and if you press buttons indicated in the second procedure, the menu item is executed.

- Use the following keystrokes to navigate a dialog:

- Move to Next/Previous object within dialog: UP or DOWN button.

- Change a setting within a dialog: LEFT or RIGHT button.

- Save settings and Close Dialog: MENU or OK button.

- Close Dialog without saving settings: CANCEL button.

Using navigation buttons in a Menu, Dialog, or Combo Box, cycles through the items.

Entering data into an edit box

- Enter data: Numeric buttons.

- Delete Data: CANCEL button. Press and hold for more than 2 seconds to delete all numbers you have entered.

- Save data: OK button.

Close without saving: Press the CANCEL button until the last character is deleted, then press the CANCEL button one more time. Or Press and hold the Cancel button until you hear ding sound and press the CANCEL button one more time.

Entering Text:

Please use the following method to enter text:

1. Use the Up and down arrows to change key layout among English, symbols, and numbers

2. Use the Cancel key to delete the previous character. Press and hold Cancel to clear the edit box.

3. Use the Left and Right arrows to move the cursor or insert a space. Press and hold the Left or Right arrows to move to the beginning or end of line respectively.

4. Press and hold the number 4 to insert a space.

5. Press and hold the number 7 to read the current character.

6. Press and hold the number 8 to read the current word.

7. Press and hold the number 9 to read the current line.

Note: in edit boxes which require numbers, you may not use the numeric keypad to enter symbols or letters.

## 2.10 Checking Battery Status

To check the battery status, the BookSense XT should be turned on first. Press and hold down OK button for more than 2 seconds and BookSense announces the battery status (1 to 10). If you press the OK button while charging BookSense announces “Battery charging, using AC POWER”. Note that if you charge using PC, the BookSense XT will not be operated, so the message will not be announced. You should check LED.

## 2.11 Setting Date & Time

After purchasing the BookSense XT, you will need to set the date and time. You can check the date and time using this menu in addition to pressing “DATE & TIME” button.

To set the date and time, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to the “date and time settings pull down.” Press the RIGHT, OK, or MENU button. “Check date and time, dialog” is announced.

- Press the DOWN button to move to ‘set date and time dialog.”

- Press the RIGHT, OK, or MENU button. “Enter 2 digits for month, edit box” is announced. Enter the numbers using the numeric keys.

- Press the DOWN button to move to the date edit box. “Enter 2 digits for day, edit box” is announced. Enter the number using the numeric keys.

- Press the DOWN button to move to the year edit box. “Enter 4 digits for year, edit box” is announced. Enter the number using the numeric keys.

- Press the DOWN button to and “time format” is announced. You can select either the 12-hour or 24-hour mode by pressing the LEFT or RIGHT button.

- Press the DOWN button to move to the hour edit box. “Enter 2 digits for the hour, edit box” is announced. Enter the number using the numeric keys.

- Press the DOWN button to move to the minute edit box. “Enter 2 digits for the minute, edit box” is announced. Enter the number using the numeric keys.

- Press the OK button to apply the settings. If you want to cancel the settings, press the CANCEL button.

If you select the 12-hour clock mode, you must enter a number between 1 and 12. For 24-hour clock mode, you must enter a number between 0 and 23. The default is 12-hour clock mode.

Note: From the edit box, month, day, year, hour, and minute can be checked by pressing the LEFT or RIGHT button. Press the CANCEL button to delete the previous character. If all of the characters are deleted, you will hear a beep. If you press the CANCEL button one more time after the beep, the time setting is canceled.

## 2.12 Checking Date &Time

To check date & time, you need to press “DATE & TIME” button which is located above Navigation buttons. You can check date & time anytime even the device is turned off. If you press the button while announcing, announcement will just stop.

If you want to know how to check date and time using MENU, please refer to 9.2.1 Checking Date and Time.

## 2.13 Changing Voice

BookSense XT has 2 voices, “Female (Kate)” which is the default, and “Male (Paul)”. It toggles between female and male by pressing number 5 button for more than 2 seconds. But this toggle will not work in the “Radio”. You can also change the voice from the Global Options, please refer to 9.3 Voice Settings.

## 2.14 Set sleep timer

The sleep timer will turn the unit off at a specified time regardless of what you are doing. Please follow these steps;

- Press number 4 button for more than 2 seconds.

- BookSense says “Enter the number of minutes for the sleep timer, XX, edit box” and enter the number range from 0 to 180.

Note: XX shows the remaining time of sleep timer. If sleep timer is “0”, BookSense says “off”.

- Press the OK or MENU button.

To cancel setting the sleep timer, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

Note: This toggle will not work in the “Radio.” If you enter “0” in step 2, the sleep timer will not work.

Note: Once the sleep timer is set, even if the device is active, it will shut off. If the device is not active but still on, the power save mode setting will have first priority. That means if you set 30 minutes for the sleep timer and set 5 minutes for the power save mode setting, the device is turned off after 5 minutes.

You can also set the sleep timer from the Global Options, please refer to 9.7 Set Sleep Timer.

## 2.15 Bluetooth On/Off

BookSense XT allows you to use a stereo Bluetooth headset. To use Bluetooth function, you need to turn on the Bluetooth first. It toggles between ON and OFF by pressing number 6 button for more than 2 seconds. But this toggle will not work in the “Radio.” You can also turn on the Bluetooth from the Global Options, please refer to 9.6 Bluetooth Options.

## 2.16 Hold Switch

Hold switch allows you to lock the BookSense XT. It is located at the right side of the device. Pull this switch down if you want to put the device in hold status. If the BookSense XT is on hold status, buttons will not function regardless the device is on/off. Just push up the Hold switch when you want to unlock them.

## 2.17 Marks used in BookSense XT

There are 3 type of mark in BookSense XT. They are “Mark”, “Voice memo”, and “Highlight mark.”

- Mark: It is a function to check specific point of a file. If you insert a mark at the point you want to remember, it will move to that point immediately in wherever.

- Voice memo: It is a function to insert a voice memo that is recorded by voice to specific point of a file. If you insert a voice memo at the point you want remember, it will move to that point immediately in wherever.

- Highlight mark: It is a function to underline specific point of a file. You can hear from beginning to end of section that you have set repeatedly. Also, if you insert a highlight mark at the point you want to remember, it will move to that point immediately in wherever.

## 2.18 Stop the voice

BookSense XT allows you to stop the voice when you move in file list. You can use this function when you are recognizing situation properly and further voice information is not required.

- When moving in file list: Press the CANCEL button to stop the voice information for contents of file list.

- When switching the storage device: Press the CANCEL button to stop voice while switching the storage device using 0 button.

- When checking file information: Press CANCEL button to stop voice while checking file information using 0 button in file list.

If you stop the voice, pressing the CANCEL button executes original functions that exit the current program or make a beep sound.

# 3. Using Help Mode

Help Mode has the function that gives you the instruction of operation when you press each button. Each Mode has its own Help Mode to be announced, and Help Mode is not an actual operating function.

To operate Help Mode, follow these steps.

- Press the MENU button.

- Press the UP or DOWN button and move to Help Mode.

- Then press the RIGHT, OK, or MENU button.

- Now Help Mode is operated. Once Help Mode is operated, Help Mode will instruct the function of each button whenever you press each button.

Help Mode is operated easily by pressing MENU button for more than 2 seconds. When you need to exit the help mode, you need to press MENU button one more time for more than 2 seconds.

# 4. Media

This chapter covers features that are specific to playing audio files.

## 4.1 What is supported in the Media?

The BookSense XT supports the following file types in the media.

- MP3, MP4, OGG, WAV, WMV, FLAC, WMA, ASF file format.

- Audible audio, including Format 4 and Enhanced Audio (.aa, .aax)

## 4.2 Playing Audio Files

To play audio file, you need to press MODE button changing to Media. When you turn the BookSense XT on first time, the default is Media. Default folders are shown in the Media. Please refer to 2.1 Folders used in the BookSense XT.

To play the file or folder that you want, by using the buttons explained 2.4 Navigating through Files and Folder.

### 4.2.1 Playing selecting Audio Files

You can play the specific files that you want to listen.

- Individual selection: Press number 9 button to select a file, then BookSense says ‘select”. For instance, if you want to listen to the second and fourth file only in file list, press the number 9 button at those files. Also, you can select a folder in the same way as above. Then press the PLAY or OK button to play all of the selected file or folder.

- All of items selection: Press number 7 button to select all of files, then BookSense says “All item selected”.

For instance, if you want to listen to all of items in file list, press the number 7 button at any file. Also, you can select a folder in the same say as above. Then press the PLAY or OK button to play all of items in file list.

### 4.2.2 Remembering the last position

The function of remembering the last position is different from each folder.

- AUDIO BOOKS, PODCASTS & Misc Audio: The file from these three folders, it remembers the last position automatically. If you play these folders or file inside of them, it will play from the location where you played it last time. And the default unit to move by is the time, so you can move by the specified time interval by using LEFT or RIGHT button.

- RECORD & RADIO: If the file is over 10 minutes inside of these two folders, it will play from the location where you played it last time. And the default unit to move by is the 1 track, so you can move by 1 track by using LEFT or RIGHT button.

- MUSIC: All the files which contain this folder, they don’t remember their last position. So if you want to keep the last position of the file then you need to put it into the folder that needs to be created under AUDIO BOOKS or PODCASTS. And the default unit to move by is the 1 track, so you can move by 1 track by using LEFT or RIGHT button.

Note: If you press the CANCEL button for more than 2 seconds while closing the file, it will ask you “Do you want to erase the current position? Press OK for “Yes”, press CANCLE for “No.” If you press the OK button, the BookSense XT does not remember the last position and exit the file. If you press the Cancel button, it remembers the last position and exit the file.

## 4.3 Pause

If you press the PLAY button while playing a file, the file will pause. Press the PLAY button again and it will resume playing.

## 4.4 Changing the Unit to Move By

If you want to move to the previous or next file while playing a file or while paused, you can change the unit to move by either one song or a time setting that is defined by the user. To change the unit to move by, press the UP or DOWN button to rotor through the items which are 1 track, 5 tracks, first or last track, time, time interval and preamp. After changing the unit to move by, press the LEFT or RIGHT button to move through the files with the option that you have selected.

The “Audible audio” file, ‘section” is added the unit to move by. So you can set the unit to move by ‘section” in “Audible audio” file.

## 4.5 Move by 1 track

You can change to “1 track” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next track. Default setting is “1 track” so if you want to play setting move by “1 track”, you just press the LEFT or RIGHT button to move through files.

## 4.6 Move by 5 tracks

You can change to “5 tracks” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next 5 tracks.

## 4.7 Moving to First or Last track

You can change to “first or last track” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to beginning or end of track.

## 4.8 Moving by Time

You can change to “time” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next location set as time. Please refer to 4.14 Setting Moving Mode to Time.

## 4.9 Changing preamp

You can change to “preamp” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it increases or decreases by preamp level 1. The range of preamp you can select is from -5 to +6. In AUDIO BOOKS or PODCASTS folder it is saved automatically, if you select all of items in those folders or select a sub-folder. So you do not need to change preamp when you open those folders later.

Note: “Preamp” to the unit to move by which means the volume is increased or decreased in the Media Player. So users can select the volume their preference, much louder than the maximum volume of the BookSense XT. It can adjust a volume of media file only, regardless of TTS volume.

## 4.10 Moving by Mark

If you have setup Mark in file, you can press the UP or DOWN button to change to Moving by Mark and by pressing the LEFT or RIGHT button; it shifts to previous or next Mark. Note that you cannot change to Moving by Mark if there is no Mark in the file, regardless of pressing the UP or DOWN button.

Note: Here are 3 different setting modes to move by mark.

- Mark: you will move to the location of the mark and start playing.

- Voice memo: you will move to the location of the voice memo and BookSense says voice memo that you have recorded. Then it starts playing from the location of voice memo.

- Highlight mark: you will move to the start point of the highlight mark. Then it starts playing the interval of highlight mark and pause. Every time you press the OK button, it keeps reading the interval that you have selected. To press the PLAY button, it starts playing the end of the highlight mark.

Note: If you press the CANCEL button while playing the interval, it will move to the end of the highlight mark and play.

## 4.11 Section Repetition

Section repetition allows you to play a specific part of an audio file as many times as you wish. This can be useful when learning a new language, and you need to hear the same information in a file over and over again. To set the section you want to have repeated, follow these steps:

- While playing, press the RECORD button at the point where you want to start the section.

- You will hear ‘set start point” and the file will keep playing.

- Press the RECORD button at the point where you want to end the section.

- You will hear ‘set end point” and the end point of the section is set.

Section repetition repeats the portion of the audio you have just set using the steps above. For more information on playback of the file, please refer to section 4.23.2 Playback Settings.

To stop the playback of the section, press the PLAY button. Section repetition only works within one file. If you set the start point but not the end point, the section repetition is cancelled.

## 4.12 Marks

You can insert a mark, voice memo, or highlight mark into an audio file to be able to return to that point in the file quickly. If a mark, voice memo, or highlight mark already exists, then it is possible to move to the mark as well as delete the mark. Once a mark has been inserted, the mark is stored.

You must toggle between mark, voice memo, or highlight mark, depending on which one you want to use. The following buttons are used to perform these functions.

- Number 1: Set mark, voice memo, or highlight mark. The default is set mark.

- Number 2: Move to mark, voice memo, or highlight mark.

- Number 3: Delete a specific mark, voice memo, or highlight mark. Press and hold down for more than 2 seconds to delete all the marks in the file.

- Number 9: Press number 9 button to switch to between mark, voice memo, and highlight mark.

When you press the number 9 button, ‘switch to voice memo setting” is announced. Pressing 9 again, ‘switch to highlight mark setting” is announced. The number 9 button is used as the toggle between working with mark, voice memo, and highlight mark.

### 4.12.1 Inserting a Mark

To insert mark, follow these steps:

- Press number 1 button while playing or in pause status.

- You will hear “Enter the mark number to insert, edit box.” Enter the number of the mark that you want to insert between 1~1,000.

- Press the OK or MENU button. Then “Mark has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the mark, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If you enter the number already existed and pressing the OK button, then “Mark ## already exists. Move? Yes” is announced. Press the OK or MENU button to set mark current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the mark number to insert, edit box” and you need to enter the different number. And the previous number keeps original location.

Note: In this case, if the number is used as voice memo or highlight mark, then “Voice memo ## or highlight mark ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 4.12.2 Inserting a Voice memo

To insert a voice mark while playing, you can use this function.

To insert a voice memo, follow these steps:

- Press number 9 button to switch to voice memo while playing or in pause status file.

- Press number 1 button, then ‘start voice memo recording” is announced. Start recording and press the OK button.

- Then ‘stop recording, enter the voice memo number to insert, edit box” is announced and enter the number of the voice memo that you want to insert.

- Press the OK or MENU button, then “Voice memo has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the voice memo, press the CANCEL button in step 2 before entering the OK button. Or press the CANCEL button instead of the OK button in step 4; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

Note: Voice memo only can be recorded up to 40 seconds, if it is over 40 seconds then ‘stop recording, enter the voice memo number to insert, edit box” is announced and enter the number that you want.

If you enter the number already existed and pressing the OK button, then “Voice memo ## already exists. Move? Yes” is announced. Press the OK or MENU button to set voice memo current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the voice memo number to insert, edit box” and you need to enter the different number. And the previous number keeps original location.

Note: In this case, if the number is used as mark or highlight mark, then “Mark ## or highlight mark ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 4.12.3 Inserting a Highlight mark

Highlight marks are used to define the start and the end positions of a passage for later playback. Setting highlight mark is a great way to study important passages in file.

To insert a highlight mark while playing, you can use this function.

To insert a highlight mark, follow these steps:

- Press number 9 button until you hear ‘switch to highlight mark setting” while playing or in pause status file.

- Press number 1 button, then ‘start highlight mark” is announced.

- Press the OK button when you reach the point that you prefer to end highlight mark.

- Then “End highlight mark, enter the highlight mark number to insert, edit box” is announced and enter the number of the highlight mark that you want to insert.

- Press the OK or MENU button, then “Highlight mark has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the highlight mark, press the CANCEL button in step 4 before entering the number. Or press the CANCEL button instead of the OK button in step 5; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If you enter the number already existed and pressing the OK button, then “Highlight mark ## already exists. Move? Yes” is announced. Press the OK or MENU button to set highlight mark current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the highlight mark number to insert, edit box” and you need to enter the different number. And the previous number keeps original location.

Note: In this case, if the number is used as mark or voice memo, then “Mark ## or voice memo ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 4.12.4 Moving to a Mark

If you have inserted a mark into the current file, then you can move to the location of the mark and continue playing. To move to the mark, follow these steps:

- Press number 2 button while playing or in pause status.

- You will hear “Enter the mark number to move to, edit box” is announced and enter the number of the mark that you want to move to.

- Press the OK button. Then it shifts to selected mark and play.

Note: In step 2, you can move to the mark regardless type of mark.

Note: Here are 3 different setting modes to move to.

- Mark: you will move to the location of the mark and start playing.

- Voice memo: you will move to the location of the voice memo and BookSense says voice memo that you have recorded. Then it starts playing from the location of voice memo.

- Highlight mark: you will move to the start point of the highlight mark. It starts playing the interval of highlight mark and pause. Every time you press the OK button, it keeps playing the interval that you have selected. To press the PLAY button, it starts playing the end of the highlight mark.

Note: If you press the CANCEL button while reading the interval, it will move to the end of the highlight mark and play.

But if you enter the number that does not exist, “This mark does not exist” is announced and you is returned to the playing or pause status. Or beyond the range of 1~1,000, BookSense says “Enter range from 1 to 1,000, edit box” and you need to enter the number range from 1 to 1,000.

To cancel moving to the mark, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

### 4.12.5 Deleting a Mark

If you have inserted a mark into a file, you can delete marks as needed. Refer to following steps to delete the marks:

- Press number 3 button while the file is playing or paused.

- You will hear, “Enter the mark number to delete, edit box.” Enter the number of the mark that you want to delete.

- Press the OK button. Then “Mark ## has been deleted” is announced and the file isgin playing again.

Note: In step 2, you can delete the mark regardless type of mark.

Note: In step 3, if the number is used as voice memo or highlight mark, then “Voice memo ## or highlight mark ## has been deleted” is announced.

However, if you enter the number that does not exist, “This mark does not exist” is announced and you is returned to the book. Or beyond the range of 1~1,000, BookSense says “Enter range from 1 to 1,000, edit box” and you need to enter the number range from 1 to 1,000.

To cancel deleting the mark, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers. While the file is playing or in a pause status, you can simply delete all marks in the file by pressing number 3 button for more than 2 seconds.

Note: If you delete the highlight mark while reading the interval, highlight mark is deleted and it keeps reading.

## 4.13 Adjusting the Playing Speed

While playing or in pause status, you can adjust playing speed by using numeric buttons.

Pitch might be up or down while playing MP4, OGG if sample rate is over 44,100 Hz.

Also, pitch changing could be occurred regardless of sample rate if you change playing speed while playing WMV, ASF.

### 4.13.1 Play Slower

If you want to decrease the speed, press number 4 button. Every time that you press this button, the speed decreases by 1 level. You can decrease the rate from the default level (level zero) down to minus 2.

### 4.13.2 Normal speed

If you want to return to normal speed, press number 5 button. The beep sound is announced and it returns to normal speed.

### 4.13.3 Play Faster

If you want to increase the speed, press number 6 button. Every time that you press this button, the speed increases by 1 level. You can increase the rate from the default (level zero) up to level 6.

## 4.14 Setting Moving Mode to Time

Press the UP or DOWN button to until you hear “Time.” This changes the moving mode to move by a specified amount of time. The default is 5 seconds. Press the LEFT or RIGHT button to start moving by the specified amount of time. If you want to change the time increment that is used, press the UP or DOWN button to change to “time interval” to switch the time moving unit. Every time you press the RIGHT, the BookSense XT toggles between 5, 10, or 30 seconds; 1, 3, 5, 10, 15, 20 or 30 minutes; and 1 hour. Pressing the LEFT, it toggles to opposite direction. Stop pressing the LEFT or RIGHT button when you reach the setting that you prefer. Once you set the time interval, then you need to switch to “Time” when you need to start moving by the specified amount of time.

## 4.15 Shuffle

While playing, you can select to either play according to the play list or play randomly.

The default setting is to play according to the play list. If you want to change this to random play, press the number 9 for more than 2 seconds. ‘shuffle play on” is announced. Press 9 again for more than 2 seconds. ‘shuffle play off” is announced. When “Shuffle Play” is on, BookSense plays the playlist in random order, then reshuffles the list and plays it again. You can also change the play mode by pressing the MENU button. Please refer to section 4.23.2 Playback Settings.

Note: If you play a folder under “Audio Books”, “Misc Audio” and “Podcasts”, the BookSense XT considers the files inside of these folders as one book in series; in that case the shuffle mode will not be activated even though you set the shuffle to “on.”

## 4.16 Move within a File via a Percent

While playing the file, you can move to the specific location by percent.

- Press number 8 button while playing or in pause status.

- Then “Currently at ##%, enter a percent value between 0 and 99, edit box” is announced, and enter the percent that you want to move to. Number should be entered between 0~99.

- Press the OK button. It will move to the point of the percent has been entered.

If you play the file for 100 minutes, you need to press number 8 button. And enter “10” when “Enter a percent value between 0 and 99, edit box” is announced and press the OK button. Then it is moved to the 10 minutes of the file and it keeps playing.

Note: If you press number 8 button when listening to an mp3 book in AUDIO BOOKS, Misc Audio or PODCASTS, move via the percent based on the total time its the length of all the mp3 files in the folder.

## 4.17 Repeating a File

You can select either one time or unlimited. The default is one time.

- Press number 8 button for more than 2 seconds, you will hear “Repeat on.”

- Press number 8 button one more time for more than 2 seconds. BookSense announces, “Repeat off” and return to playing the file. You can also turn repeat on or off by using the menu. Please refer to section 4.23.2.4 Repeat, for more information.

## 4.18 Equalizer Settings

BookSense XT provides 10 equalizer settings. To change the equalizer setting, press number 7 button. It cycles among Normal, Classic, Dance, Full Bass, Full Bass and Trebble, Live, Pop, Rock, Techno, and Jazz. The default is Normal. You can also set the equalizer by using the menu. Please refer to 4.23.1 Equalizer Settings for more information.

## 4.19 Saving the Playlist

To store the playlist, follow these steps:

- Press number 7 button for more than 2 seconds while playing or in pause status.

- Then ‘successfully saved playlist” is announced and keep playing.

- It can be saved as “PLAYLIST-001.m3u” in the Music Folder. By using PC you can change the file type.

You can also save the playlist from the menu. Please refer to 4.23.4 Saving the Playlist. To check playlist and to play, please refer to 4.23.3.1 My Playlist.

## 4.20 Undo & Redo in Media Player

Pressing the LEFT button for more than 2 seconds will “undo” the operation and return you to the last position before acting something. And pressing the RIGHT button for more than 2 seconds will “redo” the operation and return you to the position before acting “undo.” When you move to change the unit to move by; moving by percent, or moving by time, undo will work by pressing the LEFT button for more than 2 seconds. Undo & Redo allows you to do only 3 times.

Note: Undo and redo will not work in the Radio.

Note: In the media mode, moving by track will not work for this.

## 4.21 Checking the Information of the current file

Press number 0 button to check the file information while playing or in pause status. When you press 0, you will hear the following media information: current file name, elapsed time, total playing time, current track/total track, and whether the file is playing or paused. After announcing the information, the file will keep playing or remain paused.

Note: If you press the 0 key when listening to an mp3 book in audio books or podcasts, the total time gives you its the length of all the mp3 files in the folder.

## 4.22 Checking the Tag Information of the current file

To check the tag information while playing, follow these steps:

- Press number 0 button for more than 2 seconds. “Media info dialog, title” is announced.

- Press the UP or DOWN button to check the title, artist, album, and genre.

You can listen to each character by pressing the LEFT or RIGHT button. If you want to close the media info dialog, then press the OK or CANCEL button. The file isgin playing again.

## 4.23 Using the Menu in the Media

When you press the MENU button in the media player, you will see the following options: equalizer settings, playback settings, select playlist, save playlist, advanced options, help mode, and global options. You can use the menu in the media player while a file is playing or paused. Help mode (refer to chapter 3), global options (refer to chapter 9), and advanced options (refer to chapter 10) are used in all programs.

### 4.23.1 Equalizer Settings

You can set the equalizer settings by pressing 7 button as described in section 4.18 Equalizer Settings. To use the menu to change the settings, follow these steps:

- Press the MENU button while playing a file or in the file list.

- Press the RIGHT, OK, or MENU button when “Equalizer settings, dialog” is announced.

- “Equalizer settings dialog, equalizer mode, normal” is announced. You can move to the mode you want by pressing the LEFT or RIGHT button. This moves between normal, , classic, Dance, Full Bass, Full Bass and Trebble, Live, rock, Techno, and Jazz.

- Select the item you want and press the OK or MENU button to change the setting.

If you want to cancel the equalizer settings, press the CANCEL button in step 4.

### 4.23.2 Playback Settings

You can set a variety of options while playing when using the playback settings menu.

- Press the MENU button while playing or in the file list.

- Press the DOWN button to move to “Playback Settings, dialog.”

- Press the RIGHT, OK, or MENU button.

- “Media playback settings dialog, read file name, no, combo box” is announced.

By pressing the UP or DOWN button, you can navigate through the various options, including read file name, times to repeat the specified track, shuffle play, and repeat. You can change each option in the combo box by pressing the LEFT or RIGHT button.

After changing the value of each option to the setting that you want, press the OK or MENU button. Then “Option saved,” is announced. The BookSense XT will return to playing the file/pause status or the file list. If you press the CANCEL button instead of the OK button, the setting will not be applied and the edit box will close. To confirm the setting, press the OK or MENU button.

#### 4.23.2.1 Read File Name

You can choose if you want to hear the file name while playing a file. Follow steps 1 to 3 on section 4.23.2 Playback settings and press the UP or DOWN button to move to read file name. Then select either yes or no by pressing the LEFT or RIGHT button. If you choose yes, then the file name is spoken before playing the next song. The default setting is no. This setting will not announce the file name.

#### 4.23.2.2 Times to Repeat the Specified Track

You can set the amount of times a file will repeat as described in section 4.11: Section Repetition.

To set how many times a file will repeat, follow these steps:

- Please refer to section 4.23.2 Playback settings. Move to “Times to repeat the specified track, combo box.” The default is three.

- Select the value from 1 to 10 or unlimited by pressing the LEFT or RIGHT button. If you select unlimited, the BookSense XT will play the track continuously until you press the PLAY button.

Note: This function will only work if you set a portion of a file for section repetition. This setting does not affect repeating an entire file, as described in section 4.23.2.4 Repeat.

#### 4.23.2.3 Shuffle Play

You can set shuffle to on or off by pressing number 9 button as described in section 4.15 Shuffle. To set the shuffle play, follow these steps:

- Please refer to section 4.23.2: Playback settings and move to the ‘shuffle play, off combo box” by pressing the UP or DOWN button. The default is set to off.

- Select either shuffle on or off by pressing the LEFT or RIGHT button.

- Press the OK or MENU button to save the change or CANCEL if you do not want to save the change.

#### 4.23.2.4 Repeat

You can set it to play all of the files on the playlist one time or more than one time by pressing number 8 button as described in section 4.17 Repeating a File. To repeat, follow these steps:

- Please refer to 4.23.2 Playback Settings and move to “Repeat Off, combo box” by pressing UP or DOWN button.

- Select either “On” or “Off” by pressing the LEFT or RIGHT button.

- Press the OK or MENU button to save the setting.

### 4.23.3 Select Playlist

Select playlist includes the following options: my playlist, artist, album, and genre. You can move through these options by pressing the UP or DOWN button.

#### 4.23.3.1 My Playlist

To play the saved list from section 4.23.4 Saving the Playlist, follow these steps:

- Press the MENU button.

- Press the UP or DOWN button to move to ‘select playlist, pull down,” and press the RIGHT, OK, or MENU button.

- BookSense announces, “My playlist, dialog.” Press the RIGHT, OK, or MENU button.

- “My playlist dialog box, my playlist” is announced. (File name: PLAYLIST-001.m3u, PLAYLIST-002.m3u, etc) If you changed file name in PC, then that file name will appear in the list.)

- Press the UP or DOWN button to move to playlist that you want to play. Then press the OK or MENU button.

- It will automatically play the list that you have saved.

If you have not saved any playlist, in step 4, “No playlist” is announced.

Note: You can delete the file from “my playlist.” In step 5, if you press number 3 button for more than 2 seconds, BookSense says “Delete (file name)? Yes” then you need to press the OK or MENU button to delete the file. To cancel deleting, press the LEFT or RIGHT to change to “NO” then press the OK or MENU button.

#### 4.23.3.2 Search File List using Tags

The BookSense XT lets you use tags with audio files, which includes the title, artist, album, genre, etc of the audio file. When analyzing this tag, you can search for the music that you want to listen to by artist, album, or genre. You can only search for files in the music folder. If there is no tag for the file, the tag will appear as unknown. Also, if the tag does not exist or is not correct, you can edit the tag information using the media player on your PC. Each media player is different, so please refer to your medial player manual for information on how to adjust the tag information.

##### 4.23.3.2.1 Search by Artist

If you want to listen to the songs according to the artist, follow these steps:

- Press the MENU button and BookSense says “Equalizer setting, dialog.”

- Press the UP or DOWN button to move to ‘select playlist, pull down.” Press the RIGHT, OK, or MENU button.

- You will hear, “My playlist, dialog.” Press the DOWN button to move to “Artist, dialog” and press the RIGHT, OK, or MENU button.

- You will hear, “Artist list, dialog box (Name of artist- number of files) list box.” Press the UP or DOWN button to change the artist.

- Press the OK or MENU button.

Note: If the audio file does not have any tag information, the audio file is shown as “Unknown.”

##### 4.23.3.2.2 Search by Album

If you want to listen to the songs according to which album they are on, follow these steps:

- Press the MENU button

- Press the UP or DOWN button to move to ‘select playlist, pull down.” Press the RIGHT, OK, or MENU button.

- You will hear, “My playlist, dialog.” Press the DOWN button to move to “Album, dialog” and press the RIGHT, OK, or MENU button.

- BookSense announces, “Album list dialog box (Name of album- number of files) list box.” Press the UP or DOWN button to change the album.

- Press the OK or MENU button.

Note: If the audio file does not have any tag information, the audio file is shown as “Unknown.”

##### 4.23.3.2.3 Search by Genre

If you want to listen to the songs according to a specific genre, follow these steps:

- Press the MENU button

- Press the UP or DOWN button to move to ‘select playlist, pull down.” Press the RIGHT, OK, or MENU button.

- You will hear, “My playlist, dialog.” Press the DOWN button to move to “Genre, dialog” and press the RIGHT, OK, or MENU button.

- You will hear, “Genre list, dialog box (Name of genre- number of files) list box.” Press the UP or DOWN button to change genre.

- Press the OK or MENU button.

Note: If the audio file does not have any tag information, the audio file is shown as “unknown.”

### 4.23.4 Saving the Playlist

To save play list, follow these steps:

- Press the MENU button.

- By pressing the UP or DOWN button, move to ‘save playlist” and press the RIGHT, OK, or MENU button.

- Then ‘successfully saved playlist” is announced.

### 4.23.5 Mark information

This menu only appears in the menu if you open a file that has a mark, voice memo, or highlight mark. To hear mark information, follow these steps:

- Press the MENU button and “Equalizer setting, dialog” is announced.

- Press the DOWN button to move to “Mark info, dialog.” And press the RIGHT, OK, or MENU button.

- Then “Mark information, mark ##, ## hour(s) ## minute(s) ## second(s) x/y” is announced.

- Mark: “Mark ##, ## hour(s) ## minute(s) ## second(s) x/y.

- Voice memo: “Voice memo ##, ## hour(s) ## minute(s) ## second(s) x/y, voice memo recording”

- Highlight mark: “Highlight mark ##, ## hour(s) ## minute(s) ## second(s) x/y

Note: “## hour(s) ## minute(s) ## second(s)” is the position of the mark, x is current location, and y is total number of mark, voice memo, or highlight mark.

- Press the UP or DOWN button to move to check mark, voice memo, or highlight mark. If you press the OK button, you will move to the location of the mark, voice memo, or highlight mark and start playing. At this time, if you press number 3 button for more than 2 seconds, you can delete all the marks. To exit the menu, press the CANCEL button and it will return to the last position of the file before you access the menu.

### 4.23.6 Add to alarm Melody

You may wish to use the currently playing track as your alarm sound when you wake up in the morning. To do this, you must first add the currently playing track as an option in your available alarm melodies. To do this, do the following:

- Press the Menu key.

- You are placed on the option “Add to Alarm Melody”.

- Press “OK” to add the currently playing track to your alarm melody options.

# 5. DAISY

The DAISY player plays DAISY content, such as books from NLS, Bookshare, and more.

## 5.1 What is supported in the DAISY Player

The BookSense XT supports the following file types of books in the DAISY player.

- DAISY 2.0/2.02/3.0, DAISY XML/Digital Talking Book.

- ANSI/NISO Z39.86 2002, 2005.

- NLS contents. (3gp, AMR-WB+)

- RFB&D contents. (DAISY AudioPlus)

- Bookshare.org DAISY contents.

- NIMAS 1.1

- DRM: supports 2006 PDTB2 authentication.

- System Access Mobile Network content from Serotek.

- Archive (open library)

## 5.2 How to play DAISY content

If you want to play DAISY books, switch to the DAISY mode by pressing the MODE button. The first item in the DAISY file list is spoken and you can navigate through the files and folders in the DAISY folder. Move to the book that you would like to play in the file list using the buttons which were described in section 2.4: Navigating through Files and Folders. You can play a DAISY book by pressing the PLAY or OK button on the folder that contains the book.

If you connect a USB drive such as an NLS cartridge containing a DAISY book on the root of the drive, the BookSense automatically plays the DAISY book when the cartridge is connected.

If you play a book that you read previously, you will return to the last position you were when you stopped reading the book.

If you want to stop playing the current book and play a different book, press the CANCEL button. This will move you back to the file list. Move to a new book in the list and press the OK or PLAY button to play the new content.

Note: If you press the CANCEL button for more than 2 seconds while closing the book, it will ask you “Do you want to erase the current position? Press OK for “Yes”, press CANCLE for “No.” If you press the OK button, the BookSense XT does not remember the last position and exit the file. If you press the Cancel button, it remembers the last position and exit the file.

## 5.3 Pause

If you press the PLAY button again, the book will pause. Press the PLAY button one more time to resume playing.

## 5.4 Changing the Unit to Move By

You can change the unit to move by move to the previous or next paragraph, heading, or level while playing a DAISY book. To change the unit to move by, press the UP or DOWN button to toggle between paragraph, heading, beginning/end, time interval, time, preamp, mark, level 1 to level 6, page and phrase. After changing the unit to move by, press the LEFT or RIGHT button to move to the previous or next unit. Mark, time interval, time and page is announced as an option only if the book you are currently playing contains marks, time, or pages. Some books are not marked with this information, so the BookSense XT cannot move there if the book has not been correctly marked. It will move from level 1 to level 6 if the book contains those levels. In other words, if the book you are listening to only has level 1 and level 2, then you will not be given the option to move to levels 3 through 6.

Note: The default of the unit to move by is time for the audio daisy book and paragraph for the text daisy book.

## 5.5 Moving by Phrase

You can change to “Phrase” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous phrase or next phrase. Please be noted that phrase is different from content and it is up to the content producer. In the other words, one sentence can be phrased and about 5 sentences can be phrased.

## 5.6 Moving by Paragraph

You can change to “Paragraph” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next paragraph.

## 5.7 Moving by Heading

You can change to “Heading” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next Heading.

## 5.8 Moving to Beginning or End of book

You can change to “Beginning or End of book” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to first or last heading.

## 5.9 Moving by Time

You can change to “Time” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next location set as time. Please refer to 5.17 Setting the Moving Mode to Time.

Note: If there is no “time” information, moving by time won’t be shown unit to move by.

## 5.10 Changing preamp

You can change to “preamp” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it increases or decreases by preamp level 1. The range of preamp you can select is from -5 to +6. It is saved automatically if the file is Audio Daisy type. So you do not need to change preamp when you open the file later.

Note: “Preamp” to the unit to move by which means the volume is increased or decreased in the Daisy player. So users can select the volume their preference, much louder than the maximum volume of the BookSense XT.

## 5.11 Moving by Mark

If you have setup Mark in content, you can press the UP or DOWN button to change to Moving by Mark and by pressing the LEFT or RIGHT button, it shifts to previous or next Mark. Note that you cannot change to Moving by Mark if there is no Mark in the content, regardless of pressing the UP or DOWN button.

Note: Here are 3 different setting modes to move by mark.

- Mark: you will move to the location of the mark and start reading.

- Voice memo: you will move to the location of the voice memo and BookSense says voice memo that you have recorded. Then it starts reading from the location of voice memo.

- Highlight mark: you will move to the start point of the highlight mark. Then it starts reading the interval of highlight mark and pause. Every time you press the OK button, it keeps reading the interval that you have selected. To press the PLAY button, it starts reading the end of the highlight mark.

Note: If you press the CANCEL button while reading the interval, it will move to the end of the highlight mark and read.

## 5.12 Moving by Level

Moving by level will allow you to move anywhere from level 1 to level 6. If the current file has levels 1 through 3, then level 1, level 2, and level 3 is spoken as a unit to move by when you press the UP or DOWN button to change the unit to move by. If the current book contains levels 1 through 6, then the BookSense XT announces from level 1 to level 6 on the unit to move by when you press the UP or DOWN button to change the unit to move by. Select the level that you want to move to by pressing the UP or DOWN button. Then if you press the LEFT or RIGHT button, you is taken to the previous or next level. If level 3 was selected, then you can move to any level included level 1 and 2, by pressing the LEFT or RIGHT button.

## 5.13 Moving by Page

You can change to “Page” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next page.

Note: If there is no “page” information, moving by page won’t be shown as unit to move by.

## 5.14 Additional units to Move by

You can use additional units of movement in text daisy contents. Press the UP or DOWN button to toggle the unit to move by between ‘sentence”, “Word”, “Character”, “Phonetic”, and ‘search word.” These additional the unit to move by follows “Heading”. To move by mode, press the LEFT or RIGHT button while the file is playing or paused.

If you move by other modes, such as sentence mode, pressing the LEFT or RIGHT button will stop reading after the next sentence. It will continue to read when you press the PLAY button. ‘search word” is to find other instances of the same word by pressing the LEFT or RIGHT button. While reading a file, if you want to search the same word, you need to press the UP or DOWN button to change to ‘search word.” And press the LEFT to find toward the top and press the RIGHT to find toward the bottom of the file.

You can also activate the “Search Word” command by pressing the number 8 for more than 2 seconds.

When the “Search Word” dialog is opened, you are placed in an edit box containing the word currently under the reading cursor. You can press the OK key to search for the next instance of that word, or type another in the edit box. To type a search word in to the edit box, please use the text entry method described in section 2.9 of this manual.

## 5.15 Marks

You can insert a mark, voice memo, or highlight mark into a book to be able to return to that point in the file quickly. If a mark, voice memo, or highlight mark exists, then it is possible to move to the mark as well as delete the mark. Once a mark has been inserted, the mark is stored. Even if you cancel playing the book, the mark information will not be deleted. You can insert, delete, and move to a mark, voice memo, and highlight mark. You must toggle between mark, voice memo, or highlight mark, depending on which one you want to use. The following buttons are used to perform these functions.

- Number 1: Set mark, voice memo, or highlight mark. The default is set mark.

- Number 2: Move to a mark, voice memo, or highlight mark.

- Number 3: Delete a specific mark, voice memo, or highlight mark. Press and hold down for more than 2 seconds to delete all the marks in the file.

- Number 9: Press number 9 button to switch to between mark, voice memo, and highlight mark. Note that if the file consists of audio + text daisy, pressing for more than 2 seconds allows you to switch between audio and text.

When you press the number 9 button, ‘switch to voice memo setting” is announced. Pressing 9 again, ‘switch to highlight mark setting” is announced. The number 9 button is used as the toggle between working with mark, voice memo, and highlight mark.

If the file consists of audio + text daisy, pressing for more than 2 seconds allows you to switch between audio and text. After pressing 9 for more than 2 seconds when it is audio, the BookSense XT says “text” that means it switches from audio to text. And pressing 9 for more than 2 seconds allows you back to “audio”. If the Daisy book has only either text or audio, the BookSense XT says “Not allowed”.

### 5.15.1 Inserting a Mark

“Inserting Mark” will mark the current location in the file that you are playing. Refer to the following steps to insert a mark:

- Press number 1 button while playing or in pause status to insert the mark.

- You will hear “Enter the mark number to insert, edit box.” Enter the number of the mark that you want to insert between 1~1,000.

- Press the OK or MENU button. Then “Mark has been inserted.” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the mark, press CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If you enter the number already existed and pressing the OK button, then “Mark ## already exists. Move? Yes” is announced. Press the OK or MENU button to set mark current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the mark number to insert, edit box” and you need to enter the different number. And the previous number keeps original location.

Note: In this case, if the number is used as voice memo or highlight mark, then “Voice memo ## or highlight mark ## already exists, Move? Yes” is announced.

Note: In text daisy contents, only one mark can be inserted for each phrase. If you try to insert current phrase that already has mark, then “Mark ## exists at current phrase” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 5.15.2 Inserting a Voice memo

To insert a voice mark while reading, you can use this function.

To insert a voice memo, follow these steps:

- Press number 9 button to switch to voice memo while playing or in pause status file.

- Press number 1 button, then ‘start voice memo recording” is announced. Start recording and press OK button.

- Then ‘stop recording, enter the voice memo number to insert, edit box” is announced and enter the number that you want.

- Press the OK or MENU button, then “Voice memo has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the voice memo, press the CANCEL button in step 2 before entering the OK button. Or press the CANCEL button instead of the OK button in step 4; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

Note: Voice memo only can be recorded up to 40 seconds, if it is over 40 seconds then ‘stop recording, enter the voice memo number to insert, edit box” is announced and enter the number that you want.

If you enter the number already existed and pressing the OK button, then “Voice memo ## already exists. Move? Yes” is announced. Press the OK or MENU button to set voice memo current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the voice memo number to insert, edit box” and you need to enter the different number. And the previous number keeps original location. Note: In this case, if the number is used as mark or highlight mark, then “Mark ## or highlight mark ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 5.15.3 Inserting a Highlight mark

Highlight marks are used to define the start and the end positions of a passage for later playback. Setting highlight mark is a great way to study important passages in books.

To insert a highlight mark while reading, you can use this function.

To insert a highlight mark, follow these steps:

- Press number 9 button until you hear ‘switch to highlight mark setting” while playing or in pause status file.

- Press number 1 button, then ‘start highlight mark” is announced.

- Press the OK button when you reach the point that you prefer to end highlight mark.

- Then “End highlight mark, enter the highlight mark number to insert, edit box” is announced and enter the number that you want.

- Press the OK or MENU button, then “Highlight mark has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the highlight mark, press the CANCEL button in step 4 before entering the number. Or press the CANCEL button instead of the OK button in step 5; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If you enter the number already existed and pressing the OK button, then “Highlight mark ## already exists. Move? Yes” is announced. Press the OK or MENU button to set highlight mark current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the highlight mark number to insert, edit box” and you need to enter the different number. And the previous number keeps original location.

Note: In this case, if the number is used as mark or voice memo, then “Mark ## or voice memo ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 5.15.4 Moving to a Mark

If the mark, voice memo, or highlight mark has been inserted while reading a file, you can move to the location where the mark, voice memo, or highlight mark is located. Perform the following steps to move to a mark, voice memo, or highlight mark:

- Press number 2 button while the book is playing or paused.

- “Enter the mark number to move to, edit box” is announced. Enter the number of the mark that you want to move to.

- Press the OK button. You will then be taken to the place where the mark is located, and the book will start playing from that location.

Note: In step 2, you can move to the mark regardless type of mark.

Note: Here are 3 different setting modes to move to.

- Mark: you will move to the location of the mark and start reading.

- Voice memo: you will move to the location of the voice memo and BookSense says voice memo that you have recorded. Then it starts reading from the location of voice memo.

- Highlight mark: you will move to the start point of the highlight mark. It reads the interval of highlight mark and pause. Every time you press OK button, it keeps reading the interval that you have selected. To press PLAY button, it starts reading the end of the highlight mark.

Note: If you press the CANCEL button while reading the interval, it will move to the end of the highlight mark and read.

But if you enter the number that does not exist, “This mark does not exist” is announced and you is returned to the book. Or beyond the range of 1~1,000, BookSense says “Enter range from 1 to 1,000, edit box” and you need to enter the number range from 1 to 1,000.

To cancel moving to the mark, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

### 5.15.5 Deleting a Mark

Marks can be deleted as needed if the book you are playing has a mark. Follow these steps to delete the mark:

- Press number 3 button while book is playing or paused.

- “Enter the mark number to delete, edit box” is announced. Enter the number of the mark that you want to delete.

- Press the OK button. “Mark ## has been deleted” is announced and you is returned to the book.

Note: In step 2, you can delete the mark regardless type of mark.

Note: In step 3, if the number is used as voice memo or highlight mark, then “Voice memo ## or highlight mark ## has been deleted” is announced.

However, if you enter the number that does not exist, “This mark does not exist” is announced and you is returned to the book. Or beyond the range of 1~1,000, BookSense says “Enter range from 1 to 1,000, edit box” and you need to enter the number range from 1 to 1,000.

To cancel deleting the mark, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers. While the daisy book is playing or in a pause status, you can simply delete all the marks in the book by pressing number 3 button for more than 2 seconds.

Note: If you delete the highlight mark while reading the interval, highlight mark is deleted and it keeps reading

## 5.16 Adjusting Playing Speed

While a book is playing or paused, you can adjust the speed of the book by using the numbers on the keypad. It is saved automatically if the book is either Text or Audio Daisy type. So you do not need to adjust playing speed again when you open the book later.

### 5.16.1 Play Slower

If you want to decrease the speed, press the number 4 button. Every time that you press this button, the speed decreases by one level. The speed can be decreased by up to two levels.

If you are reading a DAISY book in text format, the speed is adjusted using the TTS speed, since DAISY text books are spoken by the TTS engine. The speed level ranges from 1 to 21, with the normal speed being 7. In other words, the speed can be decreased up to 6 levels from the normal speed.

### 5.16.2 Normal Speed

If you want to return to normal speed, press number 5 button. You will hear a beep and the BookSense XT will return to the normal speed.

### 5.16.3 Play Faster

If you want to increase the speed, press the number 6 button. Every time that you press this button, the speed increases by one level. The speed can be increased by up to 6 levels. If you are reading a DAISY book in text format, the speed is adjusted using the TTS speed, since DAISY text books are spoken by the TTS engine. The speed level ranges from 1 to 21 with the normal speed being 7. In other words, the speed can be increased up to 14 levels from the normal speed.

## 5.17 Setting the Moving Mode to Time

Press the UP or DOWN button to until you hear “Time.” This changes the moving mode to move by a specified amount of time. The default is 5 seconds. Press the LEFT or RIGHT button to start moving by the specified amount of time. If you want to change the time increment that is used, press the UP or DOWN button to change to “time interval” to switch the time moving unit. Every time you press the RIGHT, the BookSense XT toggles between 5, 10, or 30 seconds; 1, 3, 5, 10, 15, 20 or 30 minutes; and 1 hour. Pressing the LEFT, it toggles to opposite direction. Stop pressing the LEFT or RIGHT button when you reach the setting that you prefer. Once you set the time interval, then you need to switch to “Time” when you need to start moving by the specified amount of time.

## 5.18 Moving to a Page

While playing a DAISY book, you can move to a specific page by following these steps:

- Press number 7 button while the book is playing or paused.

- “Current page ##, total page ##, enter the page number to move to, edit box” is announced, then enter the page number that you want to move to.

- Press the OK button. The BookSense XT will then move to the page and start to play.

If you enter a number that exceeds the number of pages, then BookSense says “Entered value is not valid. Please enter a value between ## and ##, edit box.” You need to enter the valid number.

To cancel moving to the page, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If there is no page information, “There is no page information” is announced.

## 5.19 Moving to a Heading

While playing a DAISY book, you can move to a heading by following these steps:

- Press number 8 button while the book is playing or paused.

- “Current heading ##, total heading ##, enter the heading number to move to, edit box” is announced, then enter the heading number that you want to move to.

- Press the OK button. You will move to the selected heading and the book will start playing.

If you enter a number which exceeds the number of headings, then BookSense says “Entered value is not valid. Please enter a value between ## and ##, edit box” is announced. To cancel moving to the heading, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

## 5.20 Undo & Redo in DAISY Player

Pressing the LEFT button for more than 2 seconds will “undo” the operation and return you to the last position before acting something. And pressing the RIGHT button for more than 2 seconds will “redo” the operation and return you to the position before acting “undo.” When you move to change the unit to move by; moving to a paragraph, heading, beginning/end, time interval, level, page, phrase undo will work by pressing the LEFT button for more than 2 seconds. Undo & Redo allows you to do only 3 times.

Note: Undo and redo will not work in the Radio.

## 5.21 Checking the Content Information

If you want to check the content information while playing, press the number 0 for more than 2 seconds. The DAISY information dialog is announced. You can check the mark, heading, page, and total playing time through this dialog. Please refer to the following steps to check this information:

- Press number 0 button for more than 2 seconds, then “Daisy info dialog, current mark ##, total mark ##” is announced. If there’s no mark inserted in current location, “Daisy info dialog, total mark 0” is announced.

- After checking mark information, press the DOWN button. Then “heading ## of ##” is announced.

- After checking heading information, press the DOWN button. Then “page ## of ##” is announced.

- After checking page information, press the DOWN button. Then “Total time: ## hour(s) ## minute(s) ## second(s)” is announced.

- After checking total time, press the DOWN button. Then “Elapsed time: ## hour(s) ## minute(s) ## second(s)” is announced.

- After checking elapsed time, press the DOWN button. Then “Remaining time: ## hour(s) ## minute(s) ## second(s)” is announced.

When you press the UP or DOWN button in the dialog, each item is announced individually. You can listen to each character by pressing the LEFT or RIGHT button.

If you want to close the DAISY information dialog, then you need to press the OK or CANCEL button. You will then return to the book.

## 5.22 Checking the Status of the Content Information

If you want to check the status of the content information while playing a book, press number 0 button. This will allow you to check the content title, page, heading, elapsed time, and remaining time of the current book that is playing. If there is a mark inserted at the current location (phrase), you can also check the mark. You is returned to the book after the information is announced. To cancel while announcing the information, press the CANCEL button.

## 5.23 Using the Menu in the DAISY

When you press the MENU button in the DAISY player, you will see the following options: daisy playback setting, mark info (if it has mark), import CD contents (if CD-ROM is connected), advanced options, help mode, and global options. You can use the menu in the DAISY player while a file is reading or paused. Help mode (Refer to chapter 3), global options (Refer to chapter 9), and advanced options (refer to chapter 10) are used in all programs.

### 5.23.1 Play DAISY contents with audio + text file

When you play the contents with audio and text file, you can select either audio or text. To select type, please follow these steps:

- Press MENU button and “Daisy playback settings, dialog” is announced.

- Press the RIGHT, OK, or MENU button. BookSense says “Daisy playback settings dialog, daisy play type, audio, combo box.”

- Press the LEFT or RIGHT button to select audio or text.

- Press the OK or MENU button, BookSense says “Option saved” and return to the position before you access the menu.

Note: If the content with only audio, you can’t select “text.”

### 5.23.2 Reading Page Tag

If you are reading continuously, such as you might do when reading a novel, you may not wish to hear each page number spoken. You can disable “Reading Page Tag” in the “DAISY Playback Settings” menu.

- Press “Menu” from within a DAISY book.

- You are placed on “DAISY Playback Settings”, press “Menu”, “Right”, or “OK”.

- You are placed on “DAISY Play Type”, press the “Down” button to move to “Reading Page Tag”.

- Use “Left” or “Right” to enable or disable “Reading Page Tag”

- Press “OK” button to save your setting.

### 5.23.3 Mark information

This menu will only appear in the menu if you open a file that has a mark, voice memo, or highlight mark.

To hear mark information, follow these steps:

Press the MENU button and “Daisy playback settings, dialog” is announced.

- Press the DOWN button to move to “Mark info, dialog.” And press the RIGHT, OK, or MENU button.

- Then “Mark information, mark ##, ## hour(s) ## minute(s) ## second(s) x/y” is announced.

- Mark: “Mark ##, ## hour(s) ## minute(s) ## second(s) x/y

- Voice memo: “Voice memo ##, ## hour(s) ## minute(s) ## second(s) x/y, voice memo recording”

- Highlight mark: “Highlight mark ##, ## hour(s) ## minute(s) ## second(s) x/y.

Note: “## hour(s) ## minute(s) ## second(s)” is the position of the mark, x is current location, and y is total number of mark, voice memo, or highlight mark.

- Press the UP or DOWN button to move to check mark, voice memo, or highlight mark. If you press the OK button, you will move to the location of the mark, voice memo, or highlight mark and start playing. At this time, if you press number 3 button for more than 2 seconds, you can delete all the marks.

To exit the menu, press the CANCEL button and it will return to the last position of the file before you access the menu.

Note: If the file with text daisy, the position of the mark is shown as heading.

Note: If the file with audio and text daisy, the mark can be used different from playing type. That means when you select playing type as “audio”, you can only check the mark which has been inserted while playing “audio.” Also, when you select playing type as “text”, you can only check the mark which has been inserted while playing “text.” In other words, when you select playing type as “text”, you can’t check the mark which has been inserted while playing “audio.”

### 5.23.4 Import contents from CD-ROM or NLS cartridge

If you connect BookSense XT to a CD-ROM, or a USB drive such as an NLS cartridge where the DAISY book is contained in the root, you can import the contents. To import contents from a CD-ROM, or NLS cartridge, follow these steps:

- Connect the CD-ROM or USB cartridge to the BookSense XT. Please refer to 1.8 Inserting or Removing the SD CARD/USB Memory/USB CD-ROM

- Press the MENU button and “Daisy playback settings, dialog” is announced.

- Press the DOWN button to move to “Import CD contents.” And press the RIGHT, OK, or MENU button.

- BookSense says “copying” and begins copying from the CD-ROM or USB cartridge to flashdisk. BookSense announces the progress indication in increments of 10%.

- After copying, BookSense says “copy completed” and announces the title of contents.

Note: Once you start copying, you can’t cancel copying. Be cautious if the BookSense XT becomes disconnected from the CD-ROM or USB cartridge, the contents might be damaged.

# 6. Document Reader

The Document Reader allows you to read documents. It is similar to reading a file using Microsoft Word. The Document Reader also allows you to read Braille files that you have downloaded from Bookshare.

## 6.1 What is supported in the Document Reader?

The BookSense XT supports the following file types in the Document Reader:

- txt, rtf, doc, docx, html, xml, brl, brf.

- Bookshare Braille files.

- EPUB (unprotected e-book)

- Archive unprotected e-book (open library)

- PDF (Portable Document File)

## 6.2 Playing a Document File

To read a document file, you need to switch to the Document Reader. When you get into the Document Reader, you”ll see the document lists, which contain the DOCUMENTS folder. Please refer to section 2.4 Navigating through Files and Folders. Use the navigation buttons to move to the file that you want to read and press the PLAY or OK button. If you want to open a different file, then you need to press the CANCEL button. This will stop the current reading and return you to the document lists. To move to the new file, press the PLAY or OK button to read the file. Also, you can read a file that you have read recently using the menu. Please refer to section 6.21.1 Recent Documents.

Note: If you press the CANCEL button for more than 2 seconds while closing the document file, it will ask you “Do you want to erase the current position? Press OK for “Yes”, press CANCLE for “No.” If you press the OK button, the BookSense XT does not remember the last position and exit the document file. If you press the Cancel button, it remembers the last position and exit the document file.

## 6.3 Pause

If you press the PLAY button while reading the file, it stops reading. Press the PLAY button again and it will resume playing.

## 6.4 Changing the Unit to Move By

Press the UP or DOWN button to toggle the unit to move by between page, paragraph (default), line, sentence, word, character, phonetic, mark, and search word. To move by mode, press the LEFT or RIGHT button while the file is playing or paused.

Note: When moving by page or paragraph, you can navigate to a page or paragraph by pressing the LEFT or RIGHT button, but the reading will not stop.

Note: If you move by other modes, such as sentence mode, pressing the LEFT or RIGHT button will stop reading after the next sentence. It will continue to read when you press the PLAY button.

Note: If you read html file which includes heading tag, for instance level 1 through 3, then level 1, level 2, and level 3 is spoken as a unit to move by when you press the UP or DOWN button to change the unit to move by. Select the level that you want to move to by pressing the UP or DOWN button. Then if you press the LEFT or RIGHT button, you is taken to the previous or next level.

## 6.5 Moving by Page

You can change to “Page” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next page.

## 6.6 Moving by Paragraph

You can change to “Paragraph” mode by pressing UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next paragraph.

## 6.7 Moving by Heading Level

This movement is available with html files having the heading tag information.

If you read an html file which has heading tags, level 1 through 3, then level 1, level 2, and level 3 is spoken as a unit to move by when you press the UP or DOWN button.

Level corresponds to the heading tags in a file. For example, when a html file which has heading 1 and heading 2 is being played, the Level 1 and Level 2 is displayed when you press the UP or DOWN button. Press the UP or DOWN button to select the level that you want to move by. Then if you press the LEFT or RIGHT button, you is taken to the previous or next level.

## 6.8 Moving by Line

You can change to “Line” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next line.

## 6.9 Moving by Sentence

You can change to ‘sentence” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next sentence.

## 6.10 Moving by Word

You can change to “Word” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next word.

## 6.11 Moving by Character

You can change to “Character” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next character.

## 6.12 Moving by Phonetic

You can change to “Phonetic” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next phonetic.

## 6.13 Moving by Mark

You can change to “Mark” mode by pressing the UP or DOWN button. Afterwards, if you press the LEFT or RIGHT button, it shifts to previous or next mark.

Note: Here are 3 different setting modes to move by mark.

- Mark: you will move to the location of the mark and start reading.

- Voice memo: you will move to the location of the voice memo and BookSense says voice memo that you have recorded. Then it starts reading from the location of voice memo.

- Highlight mark: you will move to the starting point of the highlight mark. It reads the interval of highlight mark and pause. Every time you press the OK button, it keeps reading the interval that you have selected. To press the PLAY button, it will pause the interval.

Note: If you press the CANCEL button while reading the interval, it will move to the end of the highlight mark and read.

## 6.14 Search Word

You can change to “Word” mode by pressing the UP or DOWN button. You can search for specific words while reading the current file. To search by word, follow these steps:

- To search by word, press the number 8 for more than 2 seconds.

- You are placed in an edit box containing the word currently under your reading cursor. Press OK to search for this word, or enter a search term of your choosing.

- To enter a search term, use the numeric keys to enter text in the method described in section 2.9 of this manual. Press OK to initiate the search.

- Every time you press the RIGHT button, it will read the next line containing an instance of the word.

- Press the LEFT button and you will move to the previous line containing an instance of the word.

If there are no words that match your search, you will hear “Not found” when you press the LEFT or RIGHT button.

## 6.15 Marks

You can insert a mark, voice memo, or highlight mark into a file to be able to return to that point in the file quickly. If a mark, voice memo, or highlight mark exists, then it is possible to move to the mark as well as delete the mark. Once a mark has been inserted, the mark is stored.

You must toggle between mark, voice memo, or highlight mark, depending on which one you want to use. The following buttons are used to perform these functions.

- Number 1: Set mark, voice memo, or highlight mark. The default is set mark.

- Number 2: Move to mark, voice memo, or highlight mark.

- Number 3: Delete a specific mark, voice memo, or highlight mark. Press and hold down for more than 2 seconds to delete all the marks in the file.

- Number 9: Press number 9 button to switch to between mark, voice memo, and highlight mark.

When you press the number 9 button, ‘switch to voice memo setting” is announced. Pressing 9 again, ‘switch to highlight mark setting” is announced. The number 9 button is used as the toggle between working with mark, voice memo, and highlight mark.

### 6.15.1 Inserting a Mark

To put the mark while reading, you can use this function.

To insert mark, follow these steps:

- Press number 1 button, to insert while reading or in pause status.

- “Enter the mark number to insert, edit box” is announced and enter the number that you want.

- Press the OK or MENU button, then “Mark has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the mark, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If you enter the number already existed and pressing the OK button, then “Mark ## already exists. Move? Yes” is announced. Press the OK or MENU button to set mark current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the mark number to insert, edit box” and you need to enter the different number. And the previous number keeps original location.

Note: In this case, if the number is used as voice memo or highlight mark, then “Voice memo ## or highlight mark ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 6.15.2 Inserting a Voice Memo

To insert a voice mark while reading, you can use this function.

To insert a voice memo, follow these steps:

- Press number 9 button to switch to voice memo while reading or in pause status file.

- Press number 1 button, then ‘start voice memo recording” is announced. Start recording and press the OK button.

- Then ‘stop recording, enter the voice memo number to insert, edit box” is announced and enter the number that you want.

- Press the OK or MENU button, then “Voice memo has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the voice memo, press the CANCEL button in step 2 before entering the OK button. Or press the CANCEL button instead of the OK button in step 4; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

Note: Voice memo only can be recorded up to 40 seconds, if it is over 40 seconds then ‘stop recording, enter the voice memo number to insert, edit box” is announced and enter the number that you want.

If you enter the number already existed and pressing the OK button, then “Voice memo ## already exists. Move? Yes” is announced. Press the OK or MENU button to set voice memo current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the voice memo number to insert, edit box” and you need to enter the different number. And the previous number keeps original location. Note: In this case, if the number is used as mark or highlight mark, then “Mark ## or highlight mark ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 6.15.3 Inserting a Highlight mark

Highlight marks are used to define the start and the end positions of a passage for later playback. Setting highlight mark is a great way to study important passages in documents. To insert a highlight mark while reading, you can use this function.

To insert a highlight mark, follow these steps:

- Press number 9 button until you hear ‘switch to highlight mark setting” while playing or in pause status file.

- Press number 1 button, then ‘start highlight mark” is announced.

- Press the OK button when you reach the point that you prefer to end highlight mark.

- Then “End highlight mark, enter the highlight mark number to insert, edit box” is announced and enter the number that you want.

- Press the OK or MENU button, then “Highlight mark has been inserted” is announced and return to play or pause status.

Up to 1,000 mark, voice memo and highlight mark can be inserted and the mark number should be inserted between 1 ~ 1,000.

In step 2, when you press 1 to add a mark, the BookSense XT already has the number 1 in the edit box. Then later when you add a second mark, it already has 2 in the edit box.

If you enter the number beyond range, “Enter range from 1 to 1,000, edit box” is announced.

To cancel the insertion of the highlight mark, press the CANCEL button in step 4 before entering the number. Or press the CANCEL button instead of the OK button in step 5; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

If you enter the number already existed and pressing the OK button, then “Highlight mark ## already exists. Move? Yes” is announced. Press the OK or MENU button to set highlight mark current location. If you want to insert the different number, pressing the LEFT or RIGHT button to switch to “No” then press the OK or MENU button. It will ask you “Enter the highlight mark number to insert, edit box” and you need to enter the different number. And the previous number keeps original location. Note: In this case, if the number is used as mark or voice memo, then “Mark or voice memo ## already exists, Move? Yes” is announced.

Note: Mark, voice memo, and highlight mark are used same number so number should not be duplicated.

### 6.15.4 Moving to a Mark

If the mark, voice memo, or highlight mark has been inserted while reading a file, you can move to the location where the mark, voice memo, or highlight mark is located. Perform the following steps to move to a mark, voice memo, or highlight mark:

- Press number 2 button while you are reading a file or while it is paused.

- It will ask you “Enter the mark number to move to, edit box.” And enter the mark number that you want to move to.

- Press the OK button then and you will move to the location of the mark and start reading.

Note: In step 2, you can move to the mark regardless type of mark.

Note: Here are 3 different setting modes to move to.

- Mark: you will move to the location of the mark and start reading.

- Voice memo: you will move to the location of the voice memo and BookSense says voice memo that you have recorded. Then it starts reading from the location of voice memo.

- Highlight mark: you will move to the start point of the highlight mark. It reads the interval of highlight mark and pause. Every time you press the OK button, it keeps reading the interval that you have selected. To press the PLAY button, it starts reading the end of the highlight mark.

Note: If you press the CANCEL button while reading the interval, it will move to the end of the highlight mark and read.

But if you enter the number that does not exist, “This mark does not exist” is announced and you is returned to the document. Or beyond the range of 1~1,000, BookSense says “Enter range from 1 to 1,000, edit box” and you need to enter the number range from 1 to 1,000.

To cancel moving to the mark or voice memo, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

### 6.15.5 Deleting a Mark

When you want to delete a mark or voice memo that has been inserted, follow these steps:

- Press number 3 button while reading or in pause status.

- It will ask you “Enter the mark number to delete, edit box.” And enter the mark number that you want to delete.

- Press the OK button then “Mark ## has been deleted” is announced and return to play or pause status.

Note: In step 2, you can delete the mark regardless type of mark.

Note: In step 3, if the number is used as voice memo or highlight mark, then “Voice memo ## or highlight mark ## has been deleted” is announced.

However, if you enter the number that does not exist, “This mark does not exist” is announced and you is returned to the document. Or beyond the range of 1~1,000, BookSense says “Enter range from 1 to 1,000, edit box” and you need to enter the number range from 1 to 1,000.

To cancel deleting the mark or voice memo, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers. While the document is playing or in a pause status, you can simply delete all the marks in the document by pressing number 3 button for more than 2 seconds.

Note: If you delete the highlight mark while reading the interval, highlight mark is deleted and it keeps reading

## 6.16 Adjusting Playing Speed

While a file is playing or paused, you can adjust the playing speed by using the numbers on the keypad. It is saved automatically. So you do not need to adjust playing speed again when you open the file later.

### 6.16.1 Decrease Speed

If you want to slow down the speed, press number 4 button. Every time you press this button, the speed goes down by 1 level. The speed level ranges from 1 to 21 and normal speed is 7. In other words, the speed can be slowed down up to 6 levels.

### 6.16.2 Normal Speed

If you want to return to normal speed, press number 5 button. You will hear a beep, and the BookSense XT returns to normal speed.

### 6.16.3 Increase Speed

If you want to increase the speed, press number 6 button. Every time you press this button, the speed goes up by 1 level. The speed level ranges from 1 to 21 and normal speed is 7. In other words, the speed can be increased up to 14 levels.

## 6.17 Moving to a Page

While reading the file, you can move to a page and play.

- Press number 7 button while playing or in pause status.

- Then “current page ##, total pages ##,” “Enter the page number to move to, edit box” is announced and enter the page number.

- Press the OK button. It will move to the page and read.

If you enter the number bigger than total page, then BookSense says “Entered value is not valid. Please enter a value between ## and ##, edit box.” And you need to enter valid number. To cancel moving to the page, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

## 6.18 Moving by Percent

While reading the file, you can move to the specific location by percent.

- Press number 8 button while playing or in pause status.

- Then “Currently at ##%. Enter a percent value between 0 and 99, edit box” is announced, and enter the number from 0 to 99.

- Press the OK button. It will move to the location of percent.

If you enter the number bigger than 99, then BookSense says “Entered value is not valid. Please enter a value between 0 and 99, edit box.” And you need to enter valid number. To cancel moving by percent, press the CANCEL button in step 2 before entering the number. Or press the CANCEL button instead of the OK button in step 3; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

## 6.19 Undo & Redo in Document Reader

Pressing the LEFT button for more than 2 seconds will “undo” the operation and return you to the last position before acting something. And pressing the RIGHT button for more than 2 seconds will “redo” the operation and return you to the position before acting “undo.” When you move to change the unit to move by; moving to a page/sentence/line/sentence/word/ character/phonetic/mark undo will work by pressing the LEFT button for more than 2 seconds. Undo & Redo allows you to do only 3 times.

Note: Undo and redo will not work in the Radio.

Note: In the document reader, moving by line, sentence, word, character, phonetic will not work either.

## 6.20 Checking the Status of Content Information

If you want to check the status of content information while playing, press number 0 button. This allows you to check the file name, current page, total mark, total voice memo, and percent of current playing file. To press number 0 button while playing, it is announced the status of content information and return to current location. To cancel, press the CANCEL button.

## 6.21 Using Menu in the Document Reader

To access the menu while in the Document Reader, press the MENU button while in the Document Reader. You will see the following in the menu: Switch to Recent Documents list, Mark Info (only while reading a file or in a pause status), Page Settings (only in the document list or recent documents), advanced options, help mode, and global options. Help mode (Refer to chapter 3), global options (Refer to chapter 9), and advanced options (refer to chapter 10) are used in all programs.

### 6.21.1 Recent Documents

The Recent Documents option allows you to look at all files you have recently opened. A maximum of 20 files are stored in Recent Documents. The last file you opened is the first one in the list. If you open more than 20 files, then the oldest file is removed from the list.

- Press the MENU button and BookSense says ‘switch to Recent Documents list.” And press the RIGHT, OK, or the MENU button to select it.

- If this menu is activated, the file you are currently reading will stop and a list of recent documents will display. You can then move through the documents by pressing the UP or DOWN button and select the document that you want to read by pressing the OK button.

If you press the CANCEL button while reading from Recent Documents, you will return to Recent Documents list. If you want to return to the normal documents list, you need to press the CANCEL again.

If you want to delete Recent Documents list, press number 3 button more than 2 seconds on the file that you want to delete. BookSense says “Delete XX (file name)? Yes”, press OK or MENU button then the file is deleted.

### 6.21.2 Mark Information

This menu will only appear in the menu if you open a file that has a mark, voice memo, or highlight mark.

To hear mark information, follow these steps:

- Press the MENU button and ‘switch to Recent Documents list” is announced.

- Press the DOWN button, move to “Mark info, dialog.” And press the RIGHT, OK, or MENU button.

- Then “Mark information, mark ## position page ## of ##, ## %” is announced.

Mark: “Mark ## position page ## of ##, ## % x/y.

Voice memo: “Voice memo ## position page ## of ##, ## % x/y, voice memo recording.”

Highlight mark: “Mark ## position page ## of ##, ## % x/y.

Note: x is current location, and y is total number of mark, voice memo, or highlight mark.

- Press the UP or DOWN button to move to check mark, voice memo, or highlight mark. If you press the OK button, you will move to the location of the mark, voice memo, or highlight mark and start reading. At this time, if you press number 3 button for more than 2 seconds, you can delete all the marks. To exit the menu, press the CANCEL button and it will return to the last position of the document before you access the menu.

### 6.21.3 Page Settings

This menu only can be shown on the “Document List” and “Recent Documents.” Once you open the document, this menu will not be shown.

To set page, follow these steps:

- Press the MENU button and move to “Page settings, dialog” menu by pressing the UP or DOWN button.

- Press the RIGHT, OK or MENU button then “Page settings dialog, Characters per line 80, edit box” is announced. Enter the number that you want to change. The value is from 60 to 100, the default is 80.

- Press the DOWN button, then “Lines per page 25, edit box” is announced. Enter the number that you want to change. The value is from 18 to 40, the default is 25.

- Press the DOWN button, it will ask you “Use document form feed as separator, yes? Combo box.” Select either “Yes” or “No” by pressing the LEFT or RIGHT button.

- Then press the OK or MENU button to save options. Press the CANCEL button to cancel saving options.

# 7. Radio

To listen to the radio on the BookSense XT, please connect earphones to the earphone jack. You can listen to the radio if you do not connect earphones to the device, but the reception will not be as clear. The earphones act as an antenna for the BookSense XT.

The features of the BookSense XT radio are:

- You can listen to the radio via the internal speakers or earphones.

- You can record the radio.

- You can set 6 presets and move among the presets.

- You can search next and previous frequency.

The frequency range of the radio that you can listen to is from 87.5 MHz to 108 MHz. Please read this user manual before you start to use the radio feature.

## 7.1 Scanning to the Previous/Next Frequency

Press the LEFT button for more than 2 seconds to scan to the previous radio station.

Press the RIGHT button for more than 2 seconds to scan to the next radio station.

## 7.2 Moving to the Previous/Next Frequency by 0.1 MHz

Every time you press the LEFT button, the frequency will decrease by 0.1 MHz. If you press the RIGHT button, then the frequency will increase by 0.1 MHz. If you try to scan for a radio station, but cannot find one using the scan function, use this function to attempt to locate a radio station.

## 7.3 Jump to Specific Frequency

You can input numbers and the decimal point using the keyboard on the Booksense to jump to a specific frequency. To input a decimal point, press and hold the UP arrow for more than 2 seconds. Note: you can move to another specific frequency only if the input frequency corresponds with an existing frequency band in your city or nation. If the input frequency does not exist in your location, an error message appears and asks you to correct your input.

## 7.4 Mute/Unmute

If you press the PLAY button while listening to the radio, it is muted. Press the PLAY button one more time and then the radio will unmute.

## 7.5 Moving to the Previous/Next Added Preset

If you set presets, you can navigate through the presets. You can move to the previous preset by pressing the UP button. You can move to the next preset by pressing the DOWN button.

## 7.6 Adding Presets and Moving to Presets

To use the functions explained in section 7.4, you need to set presets. While you are listening to the radio, press the desired number from 1 to 6 for more than 2 seconds to set the preset for the station that you are listening to. For example, if you press number 1 button for more than 2 seconds while listening to a radio station on 95.7 MHz, then 95.7 MHz is set as preset 1. You can add up to 6 presets, ranging from 1 to 6.

If you try to set a preset that has already been set, the BookSense XT announces, “Preset # is already used.” and will return to the radio. You can also set presets by pressing the MENU button. Please refer to section 7.12.3.1 Adding Preset.

To move to the desired preset, you can press the UP or DOWN button as explained in section 7.4. You can also move to the desired preset by pressing the number that corresponds to the preset you want. For example, if you want to listen to a broadcast at 102.7 MHz that is set to preset 1, then simply press the number 1.

## 7.6 Changing the Frequency scanning Sensitivity

If you are not picking up radio stations using the scan function, you can adjust the sensitivity of the scan. To change the frequency scanning sensitivity, press number 7 button. You can adjust the range from 1 to 10 with the default setting being 4. The higher the number of the sensitivity, the more stations you should be able to scan to.

## 7.7 Deleting Presets

To delete a preset, follow these steps:

- Press 8 while listening to the radio.

- “Enter the preset number to delete, edit box” is announced. Enter the preset number that you want to delete.

- Press the OK button. “Preset # has been deleted” is announced.

## 7.8 Listening to the Radio via the Internal Speakers

You can listen to the radio via the internal speakers as well as the earphones. While listening to the radio, you need to press number 9 button. The BookSense XT announces, “Output radio using internal speakers, enable” and you can listen to the radio via the internal speakers. In this mode, sound will not be heard through the earphones. This allows you to continue using your earphones as an antenna while listening through the internal speakers in the BookSense XT.

If you press 9 again, the BookSense XT announces, “Output radio using internal speakers, disable” and you will hear the radio in the earphones, not from the internal speakers. While listening to the radio using the internal speakers, please do not remove the earphones from the BookSense XT, because the earphone works as a radio antenna. Listening to the radio via the internal speakers can be also set by using the MENU button. Please refer to 7.12.1 How to set the internal speakers.

## 7.9 Checking the Channel Information

If you want to hear the current station you are on while listening to the radio, press number 0 button. When you press 0 while listening to the radio it is muted. Then the BookSense XT says the frequency of the current radio station and the mono/stereo information. After announcing the information, it will return to the radio, unmute. To stop playing the status information, press the CANCEL or PLAY button and it will return to the radio, unmute.

## 7.10 Recording a Radio Broadcast

If you want to record a radio broadcast, please use the following steps:

- Press the RECORD button that is located on the right side of the device for more than 2 seconds. ‘start recording” is announced and the BookSense XT will start recording the radio.

- If you press the RECORD button again while recording, “pause recording” is announced and recording will pause. If you want to continue, press the RECORD button again. “Resume recording” is announced and it will resume recording.

- To stop the recording, press the PLAY button. ‘stop recording” is announced and the BookSense XT will stop recording and save the recorded audio file.

You can still listen to a radio station while you record it. The recorded files are saved in the RADIO folder using the following file name format: “Frequency_year_month_day_time (hour minute second).mp3.” If you recorded using a wave file instead of MP3, the file name is “Frequency_year_month_day_time (hour minute second).wav”. The number will increase if you record the same frequency broadcast again. To select the recording file format, please refer to section 7.12.2 Radio Recording Setting.

If you want to cancel the recording while recording or while the recording is paused, press the CANCEL button. “Cancel recording” is announced and the recording is canceled. You can listen to the recorded file in the media program. Once you get in the file list in RADIO folder, you will hear contents of recording about 5 seconds and file name. If you don’t want to hear preview recording, please refer to 9.4 Recording settings.

## 7.11 Adding Marks during Radio recording

BookSense XT allows you to insert a mark during Radio recording. Once you insert a mark during Radio recording, you can move to mark when you listen to recorded file.

- Press number 1 button on the position that you want to insert a mark.

- Then the mark is inserted but no message is announced.

You can insert a mark up to 20 in one recording file, and it is inserted orderly whenever you press number 1 button.

If you want to move to mark or delete a mark, please refer to 4.12.4 Moving to a Mark. 4.12.5 Deleting a Mark.

## 7.12 Using Menu in the Radio

When listening to the radio, you can access the menu by pressing the MENU button. You can set the internal speakers settings, radio recording settings, presets, frequency scanning sensitivity, advanced options, help mode, and global options. You can move among these menu items by pressing the UP or DOWN buttons. Help mode (Refer to chapter 3), global options (Refer to chapter 9), and advanced options (refer to chapter 10) are used in all programs.

### 7.12.1 How to set the Internal Speakers

This is the same function as explained in Section 7.8. To listen to the radio via the internal speakers, please follow these steps:

- Press the MENU button. “Internal speakers setting, dialog” is announced.

- Press the RIGHT, OK, or MENU button. “Internal speakers setting, dialog, Output radio using internal speakers disable, combo box” is announced.

- Press the LEFT or RIGHT button to change disable to enable. Press the OK or MENU button to confirm the change.

If you want to listen to the radio via the earphones again, follow the above procedure again and set enable to disable.

### 7.12.2 Radio Recording Settings

You can select the recording file format, sampling rate, and mono/stereo settings. To change these settings, please do the following:

- Press the MENU button.

- Press the DOWN button to move to “Radio recording settings, dialog.”

- Press the RIGHT, OK, or MENU button to enter the dialog box. “Radio recording settings dialog, recording type mp3, combo box” is announced. Press the LEFT or RIGHT button to change the recording file type to wave file.

- After selecting the recording file type, press the DOWN button. ‘sampling rate 16000 hertz, combo box” is announced. Press the LEFT or RIGHT button to select the desired sampling rate. The sampling rates can be selected from 16000Hz, 22050Hz, 24000Hz, 32000Hz and 44100Hz if you are set to record in mp3 mode. If you have selected wave file in the previous setting, sampling rates can be selected from 8000Hz, 11025Hz, 22050Hz and 44100Hz.

- After selecting the sampling rate, press the DOWN button to select the number of audio channels. “Channel stereo, combo box” is announced. Press the LEFT or RIGHT button to select mono or stereo. If you select stereo and the radio broadcast is in stereo mode, then the broadcast is recorded in stereo.

To save these settings, press the OK button. If you”d like to cancel the settings, press the CANCEL button.

### 7.12.3 Preset

You can add and delete presets using this menu.

#### 7.12.3.1 Adding Preset

As explained in Section 7.5, you can set presets using the menus. To do this, follow these steps:

- Press the MENU button.

- Press the DOWN button two times to move to preset. “Presets, pull down” is announced.

- Press the RIGHT, OK, or MENU button to select preset. “Add preset, dialog” is announced.

- Press the RIGHT, OK, or MENU button to select preset. “Add preset, dialog, select preset 1, (frequency), combo box” is announced. If there are no added channels for channel number 1, then ‘select preset 1, empty, combo box” is announced.

- Press the LEFT or RIGHT button to move to the channel number that you want to use for the frequency. Every time you move to a channel, BookSense announces the channel number and frequency. If there is an empty channel, you will hear the channel number and say “empty.”

- Move to the desired channel number and press the OK or MENU button. “Preset # has been added” is announced.

If you set a preset to a new frequency on an existing preset, “Preset # is already used” is announced. And you need to enter the different number.

#### 7.12.3.2 Deleting a Preset

To delete a preset, please follow these steps:

- Press the MENU button.

- Press the DOWN button two times to move to “Presets, pull down”.

- Press the RIGHT, OK, or MENU button. “Add preset, dialog” is announced.

- Press the DOWN button to move to “Delete preset, dialog”. Press the RIGHT, OK, or MENU button. “Delete preset, dialog, delete preset 1, (frequency), combo box” is announced. If nothing has been added to preset number 1, then “Delete preset 1, empty, combo box” is announced.

- Press the LEFT or RIGHT button to move to the preset that you want to delete.

- Press the OK button or the MENU button on the preset that you want to delete. “Preset # has been deleted” is announced and the BookSense XT will delete the old preset and return to the radio.

### 7.12.4 Adjusting the Frequency scanning Sensitivity

You can adjust the sensitivity of the scan using MENU button as well as number 7 button (Refer to Chapter 7.6).

- Press the MENU button.

- Press the DOWN button repeatedly until you hear a message ‘set Frequency scanning Sensitivity, dialog”.

- Press the RIGHT, OK, or MENU button. Then BookSense says “Channel scanning sensitivity setting dialog, Current scanning sensitivity 4, Combo box”, and you can change the level using LEFT or RIGHT buttons.

- When you press the LEFT or RIGHT buttons, the level is changed from 1 to 10.

- To complete the Frequency scanning Sensitivity setting, Press the MENU or OK buttons.

If you want to cancel settings press CANCEL button on 4 level above.

# 8. Recording

Using the BookSense XT, you can record your voice, lectures, meetings, etc. The available recording time is only limited by the free space in the internal flash memory or SD memory that you are using.

You can also record from other audio players, like CD players, cassette players or personal computers by plugging in the audio cable into the Microphone jack. You can select the recording file format among mp3, wave, or DAISY  files. The default file type is mp3. Changing the recording file type is explained in section 9.4.

Note: If the battery goes down to level 1 while recording, BookSense says “Battery low, recording process is terminated.” And if you try to record when the battery level is at 1, BookSense says “Battery is too low for recording.”

## 8.1 Recording via the Internal Microphone

By default, the BookSense XT uses an internal microphone to record. To make a voice recording, perform the following steps:

- Press the RECORD button for more than 2 seconds while using a function other than the radio. ‘start recording” is heard and the BookSense XT will start recording. Once you start recording, the media, DAISY and Document Reader will stop playing if they were being used.

- To stop recording, press the PLAY button. ‘stop, play recording? Yes” is announced. If you want to listen to the file you have recorded, press the PLAY, OK, or MENU button. The BookSense XT will play the recorded file. After it is done playing the recorded file, it will return to the function that you were using before you started recording.

- When BookSense announces ‘stop, play recording? Yes”, and you do not want to listen to the recorded file, press the LEFT or RIGHT button to change yes to no, and press the PLAY, OK, or MENU button. Then the BookSense XT will not play the recorded file and will return to the function that you were using before you started recording.

To pause the recording, press the RECORD button while recording. The BookSense XT says “pause” and it will pause the recording. Press the RECORD button again and it will resume the recording after BookSense announces, “Resume recording.”

The recorded file is saved in the RECORD folder automatically. The file name is “year_month_day_time (hour minute second).mp3”. The number is increased every time you record voices. If the record file type is set to wave file, the file name is “year_month_day_time (hour minute second).wav”.

To cancel the recording, press the CANCEL button during the recording or while you have paused the recording. Then BookSense says “Do you want to cancel recording? Press OK button for yes or press the CANCEL button for no”. Press the OK button to cancel the recording.

You can listen to the recorded file in the media program. Once you get in the file list in RECORD folder, you will hear contents of recording about 5 seconds and file name. If you don’t want to hear preview recording, please refer to 9.4 Recording settings.

## 8.2 Recording via an External Microphone

To record with an external microphone, you need to connect an external microphone to the device. After connecting the external microphone, you can record as described in section 8.1 Recording via internal microphone. If the device is set to record via line-in mode, you need to set the recording mode to microphone and connect the microphone to the device. Please refer to section 9.4 Recording Settings.

## 8.3 Recording via Line-in

If you want to record from an external audio source like a CD player, cassette player, or personal computer, connect the output of the audio source to the microphone jack of the BookSense XT using the line-in cable. You must change the audio recording source to line-in mode. The following explains how to switch to line-in mode.

- Press the MENU button.

- Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. “Alarm settings, pull down” is announced.

- Press the DOWN button repeatedly until you hear, “Recording settings, dialog.”

- Press the RIGHT, OK, or MENU button. “Recording settings, dialog, recording type, mp3, combo box” is announced.

- Press the UP or DOWN button repeatedly to move to “Recording source, microphone, combo box.”

- Press the LEFT or RIGHT button to move to line-in and press the OK or MENU button. The dialog box will close and you will return to the function that you were using before accessing the menu.

After setting the recording mode to line-in, recording is exactly the same as the method to record via the internal microphone as explained in section 8.1: Recording via the internal microphone.

## 8.4 Adding Marks during Recording

While recording, you can add marks. For example, in a classroom, if the teacher explains a very important thing, you can add marks so that you can find those locations very easily when playing the recorded file.

To add marks while recording, press number 1 button when you want to add a mark. The mark is added automatically. When adding the mark, there is no message or announcement from the BookSense XT.

You can add up to 20 marks. When you listen to recorded files that contain marks, you can move to a mark or delete a mark as explained in sections 4.12.4 and 4.12.5.

## 8.5 Recording DAISY Books

### 8.5.1 Making a DAISY Recording

Use the following steps to create a DAISY recording:

Note: Please ensure your Recording type is set to DAISY in the “record Settings” dialog before attempting to create a DAISY recording. See section 9.4 of this manual for details on setting the recording file format.

1. Press the “Record” button in the Media, DAISY or Document Reader modes (Any mode but Radio.)

2. BookSense prompts, “Start title recording and BookSense begins recording.

3. If you are currently playing content, playback is paused. BookSense gives you 10 seconds to record the title of your DAISY book.

4. After 10 seconds, BookSense prompts, “Start heading 2 recording” and automatically creates a heading navigation point at heading level 1.

5. While recording daisy, you can insert marks, headings and phrases.

Note: when creating headings, the heading’s sub title is automatically set using the first phrase under the heading.

### 8.5.2. Pause

To pause the recording, press the “RECORD” button while recording. The BookSense announces, “pause” and pauses the recording. Press the “RECORD” button again and BookSense says, “resume recording” and continues recording.

### 8.5.3. Close

When you have finished recording, press the “OK” button and BookSense announces, “Start to build”.

When creation of the DAISY package is complete, Booksense announces, “Build end” and returns you to the mode you were using before you initiated recording.

### 8.5.4. Insert Mark

You can add up to 20 marks in a DAISY recording so that you can easily access those locations when playing the recorded DAISY book.

To add a mark while recording, press the number 1 from the position at which you want to add a mark. BookSense announces, “Mark has been inserted”, and the mark is inserted at the current position. Note: this message is announced only when you are using headphones.

You can also move to previously entered bookmarks and delete bookmarks in the same manner as described in the “Bookmarks” section of this manual.

### 8.5.5. Insert Heading

You can insert an unlimited number of headings. Please note: all headings are at level 1 in the DAISY hierarchical structure, you cannot create multiple heading levels with the BookSense DAISY recording feature.

As described above, after BookSense has been recording for 10 seconds from the start of the recording, it automatically begins recording heading 2. At this time, BookSense announces, “Start heading 2 recording”.

To insert subsequent headings, press the number 8 each time you wish to start a new heading. BookSense announces, “Start heading 3 recording”, “Start heading 4 recording”, etc.

### 8.5.6. Insert Phrases

You can insert an unlimited number of phrases under a given heading. The first phrase is automatically identified as the heading’s sub title. If you do not mark any phrases under a heading, the heading will not have a sub title. In addition, if you mark the beginning of the first phrase, but do not mark the beginning of a new phrase after recording the sub title, the sub title will be identified as everything recorded from the beginning of phrase 1 to the next marked navigation point.

To insert a phrase, press the number 3. BookSense announces “Start recording phrase number”. A paragraph consists of 5 phrases.

To record a heading’s sub title, do the following:

Press the number 3. BookSense says, “Start recording phrase 1”.

Speak the heading’s sub title, chapter name, etc.

Press number 3 again. BookSense announces, “Start recording phrase 2”.

You may, or may not wish to mark further phrases, but you must mark the beginning of phrase 1 and 2 to identify the beginning and end of the heading’s sub title.

### 8.5.7. Insert Page

You can insert an unlimited number of pages in your recorded DAISY book.

As you’ll likely wish to identify your pages by page number, etc, you can use the phrase option to record the page identification. To create a new page, do the following:

- Press 3 to start phrase recording.

- Record page identification.

- Press the number 7 to “set current phrase as page1/2/3…”

- Record the text of the page.

### 8.5.8. Play Recording

DAISY recordings are saved in the “record” folder in the “DAISY” folder. The DAISY book folders are named “title001”, “Title002”, etc, according to the order in which they are recorded.

#### 8.5.8.1. Play

Use the following steps to play a recorded DAISY file:

1. Use the “MODE” button to move to the “DAISY” mode.

2. Press the DOWN arrow to navigate to the “Record” folder in the list.

3. When your cursor is placed on the “Record” folder, press the RIGHT arrow to open it.

4. Navigate to the DAISY title you wish to play using the UP and DOWN arrows, and press the OK key to start playback.

Note: as you navigate the DAISY books your recorded titles are announced rather than the actual folder names of “Title001”, “Title002”, etc.

#### 8.5.8.2. Move to Mark/Heading/Phrase/Page

##### 8.5.8.2.1. Mark

1) Move to Mark

Perform the following steps to move to a mark:

- Press the number 2 while a file is playing or paused.

- Booksense prompts, “Enter the mark number to move to, edit box.”.

- Type the mark number and press the OK button. You are taken to the location of the mark, and playback resumes.

2) Delete Bookmark

When you want to delete a mark or voice memo that has been inserted, follow these steps:

- Press the number 3 while a file is playing or paused.

- BookSense prompts, “Enter the mark number to delete, edit box.”

- Enter the mark number you wish to delete and press the OK button. BookSense announces, “Mark ## has been deleted”and you are returned to your former status and position.

##### 8.5.8.2.2. Heading

To move to a given heading, while playing a recorded DAISY book, press the UP or DOWN arrow until you get to the “Heading” navigation option. Press “the LEFT or RIGHT arrow” according to the direction which you want to move. Press the arrow key until you reach the desired heading.

You can also move to a specific heading using the number 8. While playing a DAISY book, press the number 8 and type the number of the heading to which you want to move. BookSense moves to the heading and resumes reading.

##### 8.5.8.2.3. Phrase and Paragraph

1) Phrase

While playing a recorded DAISY book, press the UP or DOWN arrow until you get to the “phrase” navigation option. Press the LEFT or RIGHT arrow according to the direction which you want to move. Press the arrow key until you reached your desired phrase.

2) Paragraph

If you set the navigation element to “paragraph” using the UP and DOWN arrows, you can navigate by 5 phrases using the LEFT or RIGHT arrow.

##### 8.5.8.2.4. Page

While playing a DAISY recording, press the UP or DOWN arrow until you get to the “Page” navigation option. Press the LEFT or RIGHT arrow according to the direction which you want to move. Press the arrow key until you reach your desired page.

# 9. Global Options

Global Options are used to set the TTS speed, pitch, volume, date & time, alarm, etc.

You can use the global options menu in each program. First, press the MENU button for each menu and move to global options by pressing the UP or DOWN buttons. Select each setting menu by pressing the RIGHT, OK, or MENU button.

The BookSense XT supports the following settings:

- Alarm settings include review current alarm, set alarm, and delete alarm.

- Date and time settings include check date and time, and set date and time.

- Voice settings.

- Recording settings.

- Check system status.

- Bluetooth options.

- Set sleep timer.

- Power save mode setting.

- Mark alert setting.

- Format storage device.

- Set current storage device.

## 9.1 Alarm Settings

The alarm settings include review current alarm, set alarm, and delete alarm. If you have not set the alarm or have deleted the alarm, the BookSense XT displays only set alarm in the menu.

### 9.1.1 Review current Alarm

To check the set alarm, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Review current alarm, dialog.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Review current alarm dialog, current alarm time is HH/MM/ (period).”

If you have not set an alarm, the BookSense XT says, ‘set alarm, dialog” instead of “Review current alarm, dialog.” In this case, you will not hear, “Review current alarm” from the alarm settings.

### 9.1.2 Set Alarm

To set the alarm, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Review current alarm, dialog.”

- Press the DOWN button to move to ‘set alarm, dialog.” If you have not set the alarm, BookSense announces, ‘set alarm, dialog” instead of “Review, dialog.”

- Press the RIGHT, OK, or MENU button.

- When you are in the hour edit box, enter the hour by using the number keys on the keypad. Press the DOWN button to move to the “minute edit box.”

- When you are in the minute edit box, enter the minute(s). Press the DOWN button to move to the ‘select am or pm combo box.”

- When you are in the am or pm combo box, you can select either am or pm that you want by pressing LEFT or RIGHT button. Press the DOWN button to move to the “melody combo box.”

- When you are in the melody combo box, you can select the alarm melody that you want by pressing the LEFT or RIGHT button. The combo box contains the 3 default alarm melodies as well as any songs you have added as alarm melodies. The final option is “Radio”. Press the DOWN button to move to the “term combo box.”

- When you are in the term combo box, you can select the alarm period. The default is once, but you can change that by pressing the LEFT or RIGHT button to switch to Monday through Friday, Monday through Saturday, Weekend, or every day. Press the DOWN button to move to the “duration combo box.”

- When you are in the duration combo box, you can select the alarm duration. The default is 5 minutes, but can be changed by pressing the LEFT or RIGHT button to switch to 1 minute to 10 minutes.

If you have chosen a melody from your music collection “Alarm Volume” appears below “Alarm duration” Use the Left and Right arrows to adjust the alarm volume.  If you choose “Radio” “Term” and “Alarm Duration” do not appear. Rather, below the “melody” option is an edit box in to which you can type the frequency of the radio station you wish to wake up to.

Press the OK or MENU button to apply the settings. If you want to cancel the settings, press the CANCEL button.

Note: When in an edit box, hour, minute, or frequency  can be reviewed by pressing the LEFT or RIGHT buttons. Press the CANCEL button to delete the previous character. If all of the characters have been deleted, you hear a beep. If you press the CANCEL button one more time after the beep, the alarm setting is canceled.

Also note: If the alarm is set to “Radio”, when the alarm sounds, the radio will play through the internal speaker, regardless of whether headphones are connected. The radio will continue playing until a key is pressed.

### 9.1.3 Delete the Alarm

To delete the alarm, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces “Alarm settings pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Review current alarm time, dialog.”

- Press the UP or DOWN button to move to, “Delete Alarm.” Press the RIGHT, OK, or MENU button.

- “Alarm deleted” is announced and you is returned to whatever you were doing.

If you have not set the alarm, you will not see the “delete alarm” option.

## 9.2 Date and Time Settings

After purchasing the BookSense XT, you will need to set the date and time. You can check the date and time using this menu in addition to pressing the date and time button.

### 9.2.1 Check Date and Time

You can also check the date and time using the menu. When using the menu, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to date and time settings pull down. Press the RIGHT, OK, or MENU button. “Check date and time, dialog” is announced.

- Press the RIGHT, OK, or MENU button. BookSense announces “Check date and time dialog, day/MM/DD/YYYY.”

- Press the DOWN button. BookSense announces “HH/MM/ AM or PM and SS.” If you have set the date and time for 24-hour mode, it is spoken as “HH/MM and SS.”

- Press the CANCEL button once you are done checking the date and time. It will then return to where you were before accessing the menu.

### 9.2.2 Set Date and Time Notification

BookSense allows you to customize how the Date and Time are announced when you query them using the “date and Time” button. To customize the Date and Time Notification, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to date and time settings pull down. Press the RIGHT, OK, or MENU button. “Check date and time, dialog” is announced.

- Press the “Down” button to navigate to “Set Date and Time Notification”.

- Press the “Right” button to open the dialog: “Date/Time Output, Date and Time combo box” is announced.

- Use the “Left” and Right” buttons to move among the 3 options: “Date and Time”, “Date”, and “Time”.

- Pres “Menu” or “OK” to save your notification setting.

### 9.2.3 Set Date and Time

To set the date and time, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to the “date and time settings pull down.” Press the RIGHT, OK, or MENU button. “Check date and time, dialog” is announced.

- Press the DOWN button to move to ‘set date and time dialog.”

- Press the RIGHT, OK, or MENU button. “Enter 2 digits for month, edit box” is announced. Enter the numbers using the numeric keys.

- Press the DOWN button to move to the date edit box. “Enter 2 digits for day, edit box” is announced. Enter the number using the numeric keys.

- Press the DOWN button to move to the year edit box. “Enter 4 digits for year, edit box” is announced. Enter the number using the numeric keys.

- Press the DOWN button to and “time format” is announced. You can select either the 12-hour or 24-hour mode by pressing the LEFT or RIGHT button.

- Press the DOWN button to move to the hour edit box. “Enter 2 digits for the hour, edit box” is announced. Enter the number using the numeric keys.

- Press the DOWN button to move to the minute edit box. “Enter 2 digits for the minute, edit box” is announced. Enter the number using the numeric keys.

- Press the OK button to apply the settings. If you want to cancel the settings, press the CANCEL button.

If you select the 12-hour clock mode, you must enter a number between 1 and 12. For 24-hour clock mode, you must enter a number between 0 and 23. The default is 12-hour clock mode.

Note: From the edit box, month, day, year, hour, and minute can be checked by pressing the LEFT or RIGHT buttons. Press the CANCEL button to delete the previous character. If all of the characters are deleted, you will hear a beep. If you press the CANCEL button one more time after the beep, the time setting is canceled.

## 9.3 Voice Settings

To set the voice settings, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to “Voice settings, dialog.” Press the RIGHT, OK, or MENU button. BookSense announces, “Voice settings dialog, volume 16, combo box.” Press the LEFT or RIGHT button to select from 1 to 21.

- Press the DOWN button. BookSense announces, “Rate 7, combo box.” Press the LEFT or RIGHT button to select from 1 to 21.

- Press the DOWN button. BookSense announces, “Pitch 8, combo box.” Press the LEFT or RIGHT button to select from 1 to 21.

- Press the DOWN button. BookSense announces, “Voice female, combo box.” Press the LEFT or RIGHT button to select either female or male.

- Press the OK button to save the options. And press CANCEL button to cancel the options.

## 9.4 Recording Settings

To set the voice recording settings, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to “Recording Settings, dialog.” Press the RIGHT, OK, or MENU button. BookSense announces, “Recording settings dialog, recording type mp3, combo box.” Press the LEFT or RIGHT button to change to wave or DAISY format.

- After selecting the recording type, press the DOWN button. “Recording Source microphone” is spoken. Press the LEFT or RIGHT button to change to either microphone or line-in.

- Press the DOWN button to move to ‘sampling rate 44100, combo box”. Select either WAV (8000 to 44100 Hz) or MP3 (16000 to 44100 Hz) by pressing the LEFT or RIGHT button.

- Press the DOWN button to move to “channel stereo, combo box.” Select either mono or stereo by pressing the LEFT or RIGHT button.

- Press the DOWN button to move to “microphone sensitivity 1, combo box.” This is the option that controls the sensitivity of the external microphone. Press the LEFT or RIGHT button to select from 1 to 4.

- Press the DOWN button to move to “preview recordings on, combo box.” This is the option that you can select either “on” or “off”.

- Press the DOWN button to move to “recording alert setting beep, combo box”. You can select among beep, message, disabled by pressing the LEFT or RIGHT button.

- Press the OK button to save the options, or press the CANCEL to cancel saving the settings.

Note: When you want to record in stereo, you must use an external microphone. The option must also be set to external microphone. And, the external microphone must be a stereo microphone.

## 9.5 Check System Status

To check the system status, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the DOWN button to move to “check system status dialog.” Press the RIGHT, OK, or MENU button and BookSense announces “Check system status dialog, battery level ##.” When charging the battery, BookSense announces, “Battery charging, using AC power.”

- After checking the battery level, press the DOWN button. BookSense announces “Flashdisk free space (number) GB, Total space (number) GB.”

- Press the DOWN button to check the firmware version and date.

- Press the DOWN button to check the key number. It will read, “Key number ##.”

- Press the OK or the CANCEL button to exit the system status menu.

Note: If the SD card or USB stick memory is connected, then you can also check each free space and total space in step 4.

Note: You can check the system status by pressing the UP or DOWN button and check each character by pressing the LEFT or RIGHT button.

## 9.6 Bluetooth Options

The BookSense XT allows you to use a stereo Bluetooth headset. Also enables to transfer data files from PC with Bluetooth to the BookSense XT using FTP service. The Bluetooth settings include the following:

### 9.6.1 Turning on Bluetooth & Connecting a Bluetooth headset

You can simply to turn on Bluetooth by pressing number 6 button for more than 2 seconds. At this time, if the BookSense XT tries to connect to the Bluetooth headset with “Connection, please wait…” message if the BookSense XT has the paired Bluetooth headset. And after connecting the headset successfully, you is heard sound from the BookSense XT. If there are more than two paired Bluetooth headsets, they is listed up from the BookSense XT. If there is no paired information, the BookSense XT will provide one list for scanning Bluetooth devices.

Using the menu to turn on Bluetooth, follow these steps:

- Assuming that Bluetooth is currently turned off, press the MENU button to access the menu.

- Press the UP or DOWN buttons to move to the “Global options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Bluetooth options, pull down” and press the RIGHT, OK, or MENU button.

- The only item listed is “Turn on Bluetooth”. Select it pressing the RIGHT, OK, or MENU button.

- Then “Bluetooth on, Bluetooth device list, scan for audio device” and press the OK, or MENU button. BookSense XT will start searching for all compatible Bluetooth devices which are in range. A beeping sound is heard during the scanning process.

- After a short delay, a list of all compatible devices that have been detected is displayed and BookSense XT announces how many devices were found.

- Assuming that your headset has been detected, press the UP or DOWN button to move to its entry on the displayed list and press the OK, or MENU button to select it. BookSense XT will ask you to enter the PIN code for your headset.

- Press the numeric button to enter the correct PIN code and press the OK button. If this is entered correctly, BookSense XT is connected to the headset and a musical jingle is heard. Shortly afterwards you should be able to hear the BookSense XT audio. This will confirm that your headset has been correctly paired with the BookSense XT.

- If at any stage, you wish to abort this process, press the CANCEL button until you exit the menu.

Note: The PIN code which is required in the above process is supplied with your headset instructions. You will need this code to complete the connection process. Many headsets use the code “0000” but you should double check this for your own headset.

Note: It is highly recommended that you use a Bluetooth 2.0 headset as headsets compatible with earlier Bluetooth versions may experience interruptions in the audio stream.

### 9.6.2 Connecting a Bluetooth headset

To connect to a Bluetooth headset if you exit the menu while Bluetooth is on, then follow these steps:

- First turn on BookSense XT’s Bluetooth facility, as detailed above.

- Ensure that the Bluetooth headset itself is turned on. It may also be necessary to switch the headset to pairing mode. You should consult your headset instructions to find out how to do this.

- On the BookSense XT, press the MENU button to access the menu.

- Press the UP or DOWN button to move to the “Global options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN button to move to the “Bluetooth options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN button to move to the “Connect headset, dialog” and press the RIGHT, OK, or MENU button.

- Then “Bluetooth device list, scan for audio device” and press the OK, or MENU button. BookSense XT will start searching for all compatible Bluetooth devices which are in range. A beeping sound is heard during the scanning process.

- After a short delay, a list of all compatible devices that have been detected is displayed and BookSense XT announces how many devices were found.

- Assuming that your headset has been detected, press the UP or DOWN button to move to its entry on the displayed list and press the OK, or MENU button to select it. BookSense XT will ask you to enter the PIN code for your headset.

- Press the numeric button to enter the correct PIN code and press the OK button. If this is entered correctly, BookSense XT is connected to the headset and a musical jingle is heard. Shortly afterwards you should be able to hear the BookSense XT audio. This will confirm that your headset has been correctly paired with the BookSense XT.

- If at any stage, you wish to abort this process, press the CANCEL button until you exit the menu.

Note: The PIN code which is required in the above process is supplied with your headset instructions. You will need this code to complete the connection process. Many headsets use the code “0000” but you should double check this for your own headset.

Note: It is highly recommended that you use a Bluetooth 2.0 headset as headsets compatible with earlier Bluetooth versions may experience interruptions in the audio stream.

### 9.6.3 FTP Service

BookSense XT allows you to use Bluetooth “FTP Service.” You can transmit and receive a file between PC and BookSense XT

Follow these steps to using “FTP Service”:

- Press the number 6 button more than 2 seconds to turn on the Bluetooth in Media Player, Document Reader, and Daisy player (except Radio mode).

- Then “Connect headset, dialog” is announced. Press CANCEL button to close this dialog.

- Scan a BookSense XT Bluetooth using the Bluetooth management program in a PC.

- Search a BookSense XT among the devices list that is scanned in a PC. BookSense XT is displayed as “BOOKSENSE”.

- Select to “BOOKSENSE” and executes the scanning a service. Then select to “FTP Service” and connect to BookSense XT.

After connecting, you can copy or delete a file in a PC and BookSense XT.

All of these steps may vary according to Bluetooth driver that is installed in a PC. So please refer to the Manual of that Bluetooth driver for the detailed information.

After completing of file transmitting, it is a better to turn off the Bluetooth of BookSense XT using number 6 button.

### 9.6.4 Turning off Bluetooth

You can also simply to turn off Bluetooth by pressing number 6 button for more than 2 seconds. Using the menu to turn off Bluetooth, follow these steps:

- Assuming that Bluetooth is currently turned on, press the MENU button to access the menu.

- Press the UP or DOWN buttons to move to the “Global options, pull down.” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Bluetooth options, pull down.” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Turn off Bluetooth.” Select it pressing the RIGHT, OK, or MENU button.

- BookSense XT will confirm that Bluetooth has been turned off and will exit the menu.

### 9.6.5 Disconnecting a Bluetooth headset

To disconnect a Bluetooth headset, follow these steps:

- Assuming that the headset has been previously connected and paired, press the MENU button to access the menu.

- Press the UP or DOWN buttons to move to the “Global options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Bluetooth options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Disconnect headset” and press the RIGHT, OK, or MENU button to select it.

- The headset is disconnected and you will exit the menu.

- You may also wish to turn off the Bluetooth facility at this stage as it reduces battery life. Follow the steps described earlier to do this.

### 9.6.6 Unpairing a headset

If you wish to unpair a headset, follow these steps:

- Assuming that the headset has been previously connected and paired, press the MENU button to access the menu.

- Press the UP or DOWN buttons to move to the “Global options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Bluetooth options, pull down” and press the RIGHT, OK, or MENU button.

- Press the UP or DOWN buttons to move to the “Unpair headset” and press the RIGHT, OK, or MENU button to select it.

- Press the UP or DOWN button to move to the headset and press the OK button that you want to unpair. If you want to unpair more than one, press the UP or DOWN to select by pressing number 9 button and press the OK button.

- The headset is unpaired and you will exit the menu.

Note: If you wish to use the headset in the future, and you have unpaired it as above, you will need to re-enter the PIN code once again.

Note: If you experience a delay in response time when using a Bluetooth headset, this is normal behavior because it is the nature of Bluetooth when using stereo Bluetooth 2.0 headsets.

## 9.7 Set Sleep Timer

To set the sleep timer, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the UP or DOWN button to move to ‘set sleep timer, dialog.” Press the RIGHT, OK, or MENU button. BookSense announces, “Enter the number of minutes for the sleep timer, XX, edit box.” You can enter the set sleep timer by pressing numeric buttons range from 0 to 180.

Note: XX shows the remaining time of sleep timer. If sleep timer is “0”, BookSense says “off.”

- Press the OK or MENU button.

To cancel setting the sleep timer, press the CANCEL button in step 3 before entering the number. Or press the CANCEL button instead of the OK button in step 4; to delete all numbers you have entered, press the CANCEL button until you have deleted all numbers. After all numbers have been deleted, you will hear a ding. Then, press the CANCEL again to close the edit box. Note that the CANCEL button acts as a backspace key and you cannot cancel out of an edit box until you delete all numbers.

Note: If you enter “0” in step 3, the sleep timer will not work. You can also press number 4 button for more than 2 seconds to set the sleep timer. This allows you to set on the fly without using the menu.

Note: Once the sleep timer is set, even if the device is active, it will shut off. If the device is not active but still on, the power save mode setting will have first priority. That means if you set 30 minutes for the sleep timer and set 5 minutes for the power save mode setting, the device is turned off after 5 minutes.

Note: The difference between the sleep timer and the power saving setting is that the sleep timer will turn the unit off at a specified time regardless of what you are doing. The power save mode setting will only turn off the unit if the BookSense XT is not playing a file or not being used.

## 9.8 Power save mode settings

When the device is turned on but is not in use, it can be turned off automatically to preserve the battery life. To set the power saving time, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the UP or DOWN button to move to “power save mode settings, dialog.” Press the RIGHT, OK, or MENU button. BookSense announces, “Power save mode settings dialog, power saving time, 5 min combo box.” You can change the power saving time by pressing the LEFT or RIGHT button to select off, 5, 10, 15, or 20 minutes.

- Press the OK or MENU button. The default is 5 min.

Note: The power saving mode will not affect the device in the following instances: when playing music, listening to the radio, connecting the AC adapter, or when connected to a PC via the USB cable.

Note: If the BookSense XT battery reaches less than 5%, the BookSense XT will automatically power off with the warning message “Battery too low. Powering off”

## 9.9 Mark alert settings

Mark alert setting allows you to select alert method when you reach the mark, voice memo, or highlight mark. To set this, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm setting, pull down.”

- Press the UP or DOWN button to move to “Mark alert setting, dialog.” Press the RIGHT, OK, or MENU button. BookSense announces, “Mark alert setting dialog, announce mark position with message, combo box.” You can change the mark notification method by pressing the LEFT or RIGHT button to select message, beep, or off.

- Press the OK or MENU button. The default is message.

Note: The mark alert setting only works while playing or reading the file. If you move to the position by mark or by using number 2 button, the mark alert setting won’t work.

## 9.10 Format Storage Device

This option is to format the flashdisk, SD card, or USB stick. To format the flashdisk, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense announces, “Alarm settings, pull down.”

- Press the UP or DOWN button to move to “format storage device, pull down”. Press the RIGHT, OK, or MENU button. BookSense announces, “Format flash disk.” If an external memory card has been inserted, you can change this option to “Format SD card” or “Format USB stick” by pressing the UP or DOWN button.

- After focusing the device that you want to format, press the RIGHT, OK, or MENU button. “Do you want to format XXXX? Yes” is announced.

- Press the OK or MENU button. “All data is deleted. Continue? Yes” is spoken.

- Press the OK or MENU button to begin formatting. “Now formatting XXXX” and in a while ‘successfully formatted XXXX” is announced.

If you want to cancel formatting the drive, press the LEFT or RIGHT button to select no.

## 9.11 Set Current Storage Device

To set the current storage device, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Global options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense says “Alarm Settings, pull down.”

- Press the UP or DOWN button, move to ‘set current storage device, dialog.” Press the RIGHT, OK or MENU button. BookSense announces, ‘storage device settings dialog, current storage device: Flash disk, combo box.” You can change this to the external memory card; SD card, or USB stick if they are connected to the device by pressing the LEFT or RIGHT button.

- Press the OK button on the option that you want to use. The contents is stored in the folder that can be used on the BookSense XT. Please refer to section 2.1: Folders used in the BookSense XT.

Note: You can only change to available drives. The drives you can change to are Flash disk, SD card, or USB. Press the OK or MENU button to apply the setting. If the external memory card is not connected, you can only check Flash disk.

Note: In file list, you can also press number 0 button more than 2 seconds to switch between the current storage devices. This allows you to switch on the fly without using the menu.

# 10. Advanced options

The advanced options include as follows “Upgrade”, “Backup settings”, “Restore settings” and “effect sound settings.” This menu allows you to upgrade the firmware, backup, restore and effect sound the settings.

## 10.1 Upgrade

HIMS may, from time to time, offer newer versions of the BookSense XT firmware. You can download this firmware from www.himsintl.com. To upgrade the BookSense XT, follow these steps:

- Download the upgrade file to your PC. The file is in a zip format.

- Extract the contents of the zip file to your PC.

- In the extracted contents, you should have a file that ends with .bin. Copy the file and paste it directly to the root of an SD card.

- Connect the BookSense XT to AC power.

- Power on the BookSense XT and insert the SD card

- Press the MENU button and move to “advanced options, pull down” by pressing the UP or DOWN button.

- Press the RIGHT, OK, or MENU button. “Upgrade firmware, dialog” is announced.

- Press the OK or MENU button. “Do you want to upgrade? Yes” is announced.

- Press the OK or MENU button.

- The update will start and report that the update is being installed. The installation takes about a minute and a half.

- After the upgrade is done, the device will automatically restart.

- If you copy the wrong file or the BookSense XT cannot find the file, then “Cannot find valid firmware .bin file” is announced and the upgrade is cancelled.

## 10.2 Backup/Restore settings

This dialog allows you to backup the settings such as TTS, Alarm, page settings, recording settings, radio settings, daisy playback settings, and media playback settings etc, and to restore them manually or automatically depending on your preference.

To backup settings, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Advanced options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense says “Upgrade firmware, dialog.”

- Press the UP or DOWN button, move to “Backup/Restore settings.” Press the RIGHT, OK or MENU button.

- BookSense says, “Backup or restore: Backup combo box.” Press the DOWN arrow to move to the backup options. You can move to the “Restore” option using the RIGHT arrow.

- BookSense announces, “Backup settings dialog, select storage device: Flash disk, combo box.” You can change this to the external memory card; SD card, or USB stick if one is connected to the device by pressing the LEFT or RIGHT button.

- Press the OK or MENU button on the device that you want to backup to. BookSense says “Backing up settings, please wait” and after a few seconds “Done.”

To restore settings, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Advanced options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense says “Upgrade firmware, dialog.”

- Press the UP or DOWN button, move to “Backup/Restore settings.” Press the RIGHT, OK or MENU button. BookSense announces, “Backup or restore, Backup combo box.” Press RIGHT arrow to move to “Restore”.

- Press the DOWN arrow to move to the “Restore” options.

- BookSense prompts, “select storage device: Flash disk, combo box.” You can change this to the external memory card; SD card, or USB stick if one is connected to the device by pressing the LEFT or RIGHT button.

- Press the DOWN arrow to move to the restore type option. Use the LEFT and RIGHT arrows to move between “Auto”, “Initialize” and and “Manual”.

- Press the OK or MENU button to activate/save your restore settings. BookSense says “Restoring settings, please wait” and after a few seconds “Done, the BookSense now will reboot.” And restarts the system.

Note: if you set the restore type to “auto”, the BookSense automatically restores your settings after a reset or upgrade. If you set the restore type to “Initialize”, settings are restored to their factory defaults.

## 10.3 Effect sound settings

This setting allows you to select the following options power signal (signal, message, or disable) and warning sound (enable or disable) settings. To set effect sound settings, follow these steps:

- Press the MENU button. Press the UP or DOWN button to move to the “Advanced options, pull down.”

- Press the RIGHT, OK, or MENU button. BookSense says “Upgrade firmware, dialog.”

- Press the UP button to move to “Effect sound settings.” Press the RIGHT, OK or MENU button. BookSense announces, “Effect sound settings dialog, power signal, signal, combo box.” You can change this to “message” or “disable” by pressing the LEFT or RIGHT button.

- Press the DOWN button to move to “Warning sound, enable, combo box.” You can change this to “disable” by pressing the LEFT or RIGHT button.

- Press the OK or MENU button on the device that you want to use.

# 11. Calculator

The BookSense XT supports the calculator program like four fundamental arithmetic operations and % arithmetic operations.

## 11.1 Using the Calculator

To start using the calculator, follow these steps below.

- Press the Menu button. By pressing the Up or Down button to move to 
“Advanced options, pull down.”

- Press the Right, OK, or Menu button. BookSense says “Upgrade firmware, dialog.”

- Press the Down button to move to calculator. And press the Right, OK, or Menu button.

BookSense says ‘start calculator, 0”. Now, you can start using the calculator.

You can also press the Mode button for more than 2 seconds to execute the calculator. This allows you to execute on the fly without using the menu. To exit the calculator, press the Mode button for more than 2 seconds and BookSense says “exit calculator” and return to the status before executing the calculator.

## 11.2 Inputting and operating the four fundamental arithmetic

Following buttons are used to operate the calculator program.

- Addition: Right button

- Subtraction: Left button

- Multiplication: Up button

- Division: Down button

- Opening a parenthesis: Press the Left button for more than 2 seconds

- Closing a parenthesis: Press the Right button for more than 2 seconds

- Inputting a decimal point: Press the Up button for more than 2 seconds

- Inputting %: Press the Down button for more than 2 seconds

Using the numeric button to input the number, navigation button to input the fundamental arithmetic and you need to press Menu button to check the result. If you want to repeat the result, you need to press OK button. The Cancel button acts as a backspace key, so you can delete the number that you have entered. To delete all numbers you have entered, press the CANCEL button for more than 2 seconds.

Let’s take a look at the examples.

1) “10*(13+7)”

- Press the number 1 and 0.

- Press the Up button to input *.

- Press the Left button for more than 2 seconds to input opening a parenthesis.

- Press the number 1 and 3.

- Press the Left button to input an addition.

- Press the number 7.

- Press the Right button for more than 2 seconds to input closing a parenthesis.

- And press the Menu button.

- Then you will get the result of “200.”

2) “250+10%”

- Press the number 2, 5, and 0.

- Press the Right button to input an addition.

- Press the number 1 and 0.

- Press the Down button for more than 2 seconds to input a %.

- And press the Menu button.

- Then you will get the result of “275.” Thus it is same as 250+250*0.1.

3) “250*10%”

- Press the number 2, 5 and 0.

- Press the Up button to input a multiplication.

- Press the number 1 and 0.

- Press the Down button for more than 2 seconds to input a %.

- Press the Menu button.

- Then you will get the result of “25.” Thus it is same as 250*0.1.

## 11.3 Using the help mode of Calculator

While executing the calculator, help Mode gives you the instruction about four fundamental arithmetic operations when you press each button.

Help Mode is operated easily by pressing MENU button for more than 2 seconds. Help Mode is not an actual operating function. When you need to exit the help mode, you need to press MENU button one more time for more than 2 seconds.

# 12. Troubleshooting Guide

If you are having any trouble with the BookSense XT, please try the following suggestions to address your problem:

## 12.1 The BookSense XT will not turn on

- Check to make sure that the battery has been inserted properly into its compartment.

- If the battery is inserted properly, connect the AC adapter, and plug the AC adapter into an electrical outlet. The battery may need to be charged.

- Check the location of the Hold switch. If this switch is on lock, the BookSense XT will not be able to be turned on.

## 12.2 The BookSense XT stops responding

- Press the reset button.

- Do a hard reset

Hard Reset: While pressing 4, press and release the reset button at the same time. Continue to hold the number 4 down for an additional 20 seconds. Then, release the number 4, and then BookSense XT should reset.

- Take out the battery and reinsert the battery after 10 seconds. Wait for 30 to 60 seconds for the BookSense XT to turn on automatically.

## 12.3 Having trouble with Scanning Radio Channels

If you are not receiving any radio stations while scanning, you can increase the sensitivity of the BookSense XT to make it pick up more radio stations. To change the sensitivity of the channel scan, press number 7 button. You can adjust the range from 1 to 10 with the default setting being 4. The higher the number of the sensitivity, the more channels you can search for. It is also highly recommended that earphones are used and not the external speakers. Or, if you are using the external speakers, make sure that headphones are connected to be used as an antenna. For more information on how to do this, refer to the Radio section in this manual.

## 12.4 No sound when using Bluetooth

Please check to see if the Bluetooth headset supports A2DP, since the BookSense XT only supports A2DP. Most Bluetooth stereo 2.0 headsets support A2DP.

## 12.5 No Sound from Internal Speakers or Earphones

The BookSense XT allows you to adjust the volume for both the earphones and the internal speakers separately. When you connect earphones to the device, the volume can be adjusted for earphones. You can also adjust the volume for the internal speakers. This means that the volume is different depending upon if you are listening via earphones or the internal speakers. So if you cannot hear any sound from the earphones or the internal speakers, then you need to increase the volume while the earphones are connected to the device. If you cannot hear any sound from the internal speakers, you need to increase the volume of internal speakers when no earphones are connected to the device.

# 13. Warranty

Do not take apart the BookSense XT by yourself. Do not have anyone else who is not authorized by HIMS take apart the BookSense XT. If an unauthorized person or company disassembles the device, serious damage may occur to the BookSense XT. If an unauthorized person disassembles the BookSense XT, the warranty is void. If any liquid or external force damages the device, this is not covered by the warranty, even if the damage occurred during the warranty period. If your BookSense XT needs to be repaired, then you should contact HIMS.

# 14. Contact Information

If you have any problems with the BookSense XT, please contact the dealer you purchased your unit from. If you require further assistance, please contact us at support@hims-inc.com.

Or, you can contact HIMS by phone at 512-837-2000.

# Text boxes

Microphone jack

Ear phone jack

DATE & TIME Button

Navigation Button

MENU Button

Numeric Button

CANCEL Button

OK (Confirm) Button

LED

AC Adapter jack

USB OTG

Front

PLAY button

MODE Button

RECORD Button

VOLUME Button

Hold Switch

SD Card

RESET Button

Side